## Slide 1: Real-Time System: Introduction

## Slide 2: Introduction: Real-Time System
Real-time
  Does not denote speed/fast
  But meet the timing constraints or deadlines
Goal: make the system predictable and robust
Predictability: have deterministic behavior
  Usually use the worst-case analysis
  Guaranteed response/reaction times
Robustness: the job with granted performance will not be interfered with other job
Notes: Real-time systems denotes to meet the timing constraints of tasks.
Why we introduce the real-time system: 1. predictability 2. robustness

## Slide 3: Introduction: Real-Time System
Real-time system: respond to external events in a timely fashion and the response time is guaranteed

## Slide 4: Introduction: Real-Time System
Responding to external events includes
  Recognize when an event occurs
  Perform the required processing
  Output the result within a given time constraint
Timing constraints include
  Finish time
  Both start time and finish time

## Slide 5: Real-Time Systems
The structure of a real-time system is a controlling system and at least one controlled system
Controlling
System
Controlled
System
Controlled
System
Controlled
System
output
input
output
input

## Slide 6: Real-Time Systems (Cont.)
The controlling system interacts with the controlled system in various ways
  The interaction can be periodic
    The controlling system -> the controlled system
    Predictable and occurs at predefined intervals
  The interaction can be aperiodic
    The controlled system -> the controlling system
    Unpredictable from random occurrences of external events
  The communication can be a combination of both types
The controlling system must process and respond to the events and information generated by the controlled system in a guaranteed time frame.

## Slide 7: Real-Time Systems Examples
Real-time weapons defense system
  Controlling system
    A command-and-decision (C&D) system
  Controlled system
    A radar system
    Weapons firing control system
  Communication between the radar system and C&D system is aperiodic
  Communication between the C&D system and the weapon firing control system is periodic

## Slide 8: Real-Time Systems Examples (Cont.)
Cruise missile guidance system
  Controlling system
    Navigation system: contain digital maps covering the missile flight path
  Controlled system
    Radar system
    Divert-and-altitude-control system
  Communication between radars and the navigation system is aperidoic
  Communication between the navigation system and the diver-and-altitude-control system is periodic

## Slide 9: Real-Time Systems Examples (Cont.)
DVD player
  Controlling system
    DVD player must decode both the video and audio streams from the disc simultaneously.
  Controlled system
    Remote control is viewed as a sensor to feed pause and language selection events into DVD player

## Slide 10: Characteristics of Real-Time Systems
Characteristics
  Must produce correct computational results, called logical or functional correctness
  These computations must conclude within a predefined period, called timing correctness
The overall correctness of a real-time system depends on both the functional correctness and the timing correctness

## Slide 11: Type of Real-Time System
Hard Real-Time
Soft Real-Time
Firm
Notes: Real-time System can be classified as hard real-time system, soft real-time system and firm real-time system.

## Slide 12: Hard Real-Time System
Degree of tolerance of missed deadline
  Extremely small or zero
Usefulness of computed results after missed deadlines
  Likely useless
Severity of the penalty incurred for failing to meet deadlines
  catastrophe

## Slide 13: Hard Real-Time System
Examples:
  Nuclear reactors
  Flight controller
  Weapon defense system
  Missile guidance system
Notes: For hard-real-time system, missing tasks’ deadlines would cause catastrophic consequence. For example, nuclear reactors and flight controllers are all hard-real-time systems.

## Slide 14: Hard Real-Time System

## Slide 15: Hard Real-Time System

## Slide 16: HArd Real-Time System

## Slide 17: Hard Real-Time System

## Slide 19: Soft Real-Time System
Degree of tolerance of missed deadline
  Non-zero
Usefulness of computed results after missed deadlines
  Have a rate of depreciation
Severity of the penalty incurred for failing to meet deadlines
  Non-catastrophic

## Slide 20: Soft Real-Time System
A miss of timing constraints is undesirable. However, a few misses do no serious harm
  The timing requirements are often specified in probability terms
  The time constraints are guaranteed on a statistical basis
Examples:
  Multimedia Streaming
  Electronic games
  Quality-of-Service (QoS) guarantees
Notes: Missing a task’s deadline in a soft real-time system will only decrease the performance of the system, but not influence system’s correct behavior. For example, multimedia streaming, electronic games, and quality-of-service applications are all soft-real-time systems.

## Slide 21: Soft Real-Time System

## Slide 22: Soft Real-Time System

## Slide 23: Soft Real-Time System

## Slide 24: Comparison
Time
Value
Hard RTS
Soft RTS
Deadline
Notes: This is the comparison of hard and soft real-time systems.
X-axis denotes the time while Y-axis denotes the value.
For hard RTS, once missing deadline, the system’s value is negative, which means the system is damaged. In contrast, in a soft RTS, the value is still positive after missing deadline. However, if the finish time is far behind deadline, the value would also become negative.

## Slide 25: Job versus Task
Job: unit of work that is scheduled and executed by the system
  Computation of a FFT (Fast Fourier Transform)
  Transmission of a data packet
Task: a set of related jobs which jointly provide some system function
Notes: We assume that system activation entities consists of Job and Task.
Job denotes a set of execution flow while Tasks denotes a set of related jobs that cooperate to provide a specific system function.

## Slide 26: Release Time and Deadlines
Release time
  the instant of time at which the job becomes available for execution
  Jobs have no release time if all the jobs are released when the system begins execution
Response time
  The length of time from the release time of the job to the instant when it completes
Notes: This and following slides shows the job’s timing characteristics, including release time, response time, relative deadlines and (absolute deadline)

## Slide 27: Release Time and Deadlines (Cont.)
Relative deadline
  The maximum allowable response time of a job
Deadline or Absolute Deadline
  The instant of time by which its execution is required to be completed
  Equal to the release time plus the relative deadline
  A job has no deadline if its deadline is at infinity

## Slide 28: Feasibility
Timing Constraints
  A constraints imposed on the timing behavior of a job
  Specified in terms of
    Release time
    Relative deadline or absolute deadline
The set of rules that determines the order in which tasks are executed is called a scheduling algorithm
  A schedule is feasible if all tasks can be completed according to the timing constraints
  A set of tasks is schedulable if there exists at least one algorithm that can produce a feasible schedule

## Slide 29: Type of Tasks
A Periodic task is executed repeatly at regular time intervals, and each invocation is called a job or instance.
  Often time-driven
A Aperiodic task is executed to response to external events, and to respond, it executes aperiodic jobs whose release time are not know a priori
  Often event-driven
  Off-line guarantee of aperiodic tasks must make proper assumptions on the environments; that is, by assuming a maximum arrival rate for each event (i.e., minimum interarrival time)
    Aperiodic tasks characterized by a minimum interarrival time are called sporadic tasks
Notes: According to the regularity of task’s activation, we divide the tasks into two sets: on is the periodic task and the other is the aperiodic task.
Periodic tasks are regularly activated at a constant rate. Each invocation activity is called a job or an instance.
In contrast, the invocation of aperiodic tasks are not regular and undetermined. Thus, it is often event-driven.
Notably, since the uncertainly of tasks’ invocations, to off-line guarantee of aperiodic tasks’ execution, we may assume a maximum arrival rate for each event. A aperiodic task that is characterized by a minimum interval time is called a sporadic task.

## Slide 30: Classification of Scheduling Algorithm
Preemptive/Nonpreemptive
  Preemptive: the running tasks can be interrupted to assign the processor to another task
  Non-preemptive: A task, once started, is executed until completion.
Static/Dynamic
  Static: the scheduling decisions are based on fixed parameters and assigned to tasks before their activation
  Dynamic: the scheduling decisions are based on dynamic parameters that may change during system evolution
Notes: The scheduling algorithms can be classified as
Preemptive or nonpreemptive
Static or dynamic
Off-line or on-line
Optimal or heuristic
Dynamic or fixed

## Slide 31: Classification of Scheduling Algorithm (Cont.)
Off-line/On-line
  Off-line: a scheduling algorithm is executed on the entire task set before actual task activation. The schedule may be stored in a table and later executed by a dispatcher
  On-line: scheduling decisions are taken at runtime every time a new task enter the system or when a running task terminates

## Slide 32: Classification of Scheduling Algorithm (Cont.)
Optimal/Heuristic
  Optimal: an algorithm is optimal if it minimizes some given cost function defined over the task set.
    If no cost function is given and only concern feasibility, an algorithm is optimal if it may fail to meet deadline only if no other algorithms can meet it
  Heuristic: an algorithm is heuristic if it tends toward but does not guarantee to find the optimal schedule
Dynamic/Fixed
  Fixed: in which the priority of each process is fixed for any instantiation
  Dynamic: in contrast from above

## Slide 33: Metrics for Performance Evaluation
Metrics for hard real-time system
  Schedulability
  Optimality, etc.
Metrics for soft real-time system
  Miss ratio
  Response time, etc.
Other metrics
  Completion time
  Jitter, etc.
  Combination of metrics
Notes: To evaluate a hard real-time system, the metrics may be schedulability, optimality etc.
In contrast, to evaluate a soft real-time system, the metrics may be miss ratio, response time, etc.
Other metrics, including the completion time, jitter, may also be applied in the evaluation of a hard or soft real-time system

## Slide 34: Commonly Used Approaches to Real-Time Scheduling
Clock-Driven
Priority-Driven
Notes: The approaches to implement a real-time scheduling algorithm, depending on its characteristics, may be clock-driven or priority-driven.

## Slide 35: Clock-Driven Approach
Also called time-driven
  Because each scheduling decision is make at a specific time, independent of events, such as job releases or completions, in the system
Applicable only when the system is deterministic, except for a few aperiodic jobs
The parameters of all periodic tasks are known a priori
Therefore, the scheduler is often constructed by a static schedule of the jobs off-line
  Use a hardware timer to trigger the scheduling decision
Notes: Clock-driven approach is also called time-driven. To adopt the clock-driven approach, the system must be deterministic. For example, the scheduling algorithm for periodic tasks may use the clock-driven approach since their parameters are know a priori. As a result, the scheduler often constructed by a static schedule off time.

## Slide 36: Priority-Driven Approach
Scheduling decisions are made when events, such as release and completions of job occurs
  Therefore, priority-driven algorithms are even-driven
Many non-real-time scheduling algorithms are priority-driven
  FIFO (First-In-First-Out)
    Assign priority according to the release time
  SETF (Shortest-Execution-Time-First)
    Assign priority on the basis of job execution times
Notes: Priority-driven approach assigns each task a different priority and schedules tasks on the basis of their priority.
To assign a task’s priority, we may choose a task’s real-time or deadlines to determine its priority. Thus, priority-driven algorithms are event-driven and the event are tasks’ priority.
Some well-known priority-driven algorithms are FIFO and SETF.

## Slide 37: Priority-Driven Approach (Cont.)
Priority-driven real-time scheduling algorithms
  Dynamic-priority
    e.g. EDF (Earliest Deadline First)
  Fixed-priority
    e.g. RM (Rate Monotonic)
Notes: For real-time systems, depending on whether dynamic or fixed or not, the priority-driven approaches may be dynamic-priority or fixed-priority.
The well-known EDF algorithm is a dynamic-priority driven algorithm. In contrast the RM is a fixed-priority driven algorithm

## Slide 38: Issues of Real time OS
Race condition
Dead lock
Live lock
Starraing/Aging