## Slide 1
13-2 STANDARD ETHERNET
The original Ethernet was created in 1976 at Xerox’s Palo Alto Research Center (PARC). Since then, it has gone through four generations. We briefly discuss the Standard (or traditional) Ethernet in this section.
MAC Sublayer Physical Layer
Topics discussed in this section:

## Slide 2
Figure 13.4 802.3 MAC frame

## Slide 3
Header
Preamble / SFD: - this element within the header is added by the layer 1 part of the protocol stack. It enables the receiver to synchronise and know that a data frame is about to be sent.
Preamble (PRE) - This is seven bytes long and it consists of a pattern of alternating ones and zeros, and this informs the receiving stations that a frame is starting as well as enabling synchronisation.

## Slide 4
Start of Frame Delimiter (SFD) - This consists of one byte and contains an alternating pattern of ones and zeros but ending in two ones.
Destination Address (DA) - This field contains the address of station for which the data is intended, this can be an individual address or multiple addresses as indicated by the destination address field.

## Slide 5
Source Address (SA) - The source address consists of six bytes, and it is used to identify the sending station. This is always a single address and this is indicated within the address field. Again the MAC address is used. More details are given in the section below.
Length / Type - This field is two bytes in length. It provides MAC information and indicates the number of client data types that are contained in the data field of the frame. It may also indicate the frame ID type if the frame is assembled using an optional format.(IEEE 802.3 only).

## Slide 6
Payload
Data - This block contains the payload data and it may be up to 1500 bytes long. If the length of the field is less than 46 bytes, then padding data is added to bring its length up to the required minimum of 46 bytes.
Later implementations allowed for so-called ‘jumbo’ frames up to 9,000 bytes long to facilitate certain types of large traffic flows such as file transfers and video links.

## Slide 7
Trailer
Frame Check Sequence (FCS) - This field is four bytes long. It contains a 32 bit Cyclic Redundancy Check (CRC) which is generated over the DA, SA, Length / Type and Data fields.
After the Ethernet data frame itself there is an inter-frame gap of a minimum of 12 bytes of data. This acts as a delimiter to ensure that the receiver knows the frame is complete before any further data is sent.

## Slide 8
Figure 13.5 Minimum and maximum lengths

## Slide 9
Figure 13.6 Example of an Ethernet address in hexadecimal notation

## Slide 10
Figure 13.7 Unicast and multicast addresses

## Slide 11
The least significant bit of the first byte defines the type of address. If the bit is 0, the address is unicast; otherwise, it is multicast.
Note

## Slide 12
The broadcast destination address is a special case of the multicast address in which all bits are 1s.
Note

## Slide 13
Define the type of the following destination addresses:
a. 4A:30:10:21:10:1A b. 47:20:1B:2E:08:EE
c. FF:FF:FF:FF:FF:FF
Solution
To find the type of the address, we need to look at the second hexadecimal digit from the left.
If it is even, the address is unicast.
If it is odd, the address is multicast.
If all digits are F’s, the address is broadcast. Therefore, we have the following:
a. This is a unicast address because A in binary is 1010.
b. This is a multicast address because 7 in binary is 0111.
c. This is a broadcast address because all digits are F’s.
Example 13.1

## Slide 14
Figure 13.3 Ethernet evolution through four generations

## Slide 15
Figure 13.8 Categories of Standard Ethernet

## Slide 16
Figure 13.9 Encoding in a Standard Ethernet implementation

## Slide 17
Figure 13.10 10Base5 implementation

## Slide 18
Figure 13.11 10Base2 implementation

## Slide 19
Figure 13.12 10Base-T implementation

## Slide 20
Figure 13.13 10Base-F implementation

## Slide 21
Table 13.1 Summary of Standard Ethernet implementations

## Slide 22: Standardization of Wireless Networks
Wireless networks are standardized by IEEE.
Under 802 LAN MAN standards committee.
Application
Presentation
Session
Transport
Network
Data Link
Physical
ISO
OSI
7-layer
model
Logical Link Control
Medium Access (MAC)
Physical (PHY)
IEEE 802
standards
Notes: Same organization that came up with IEEE 802.3 Ethernet,
which is responsible for success of Internet

## Slide 23: IEEE 802.11 Overview
Adopted in 1997.
Defines;
MAC sublayer
MAC management protocols and services
Physical (PHY) layers
  IR
  FHSS
  DSSS
Goals
To deliver services in wired networks
To achieve high throughput
To achieve highly reliable data delivery
To achieve continuous network connection.

## Slide 24: Components
Station
BSS - Basic Service Set
  IBSS : Infrastructure BSS : QBSS
ESS - Extended Service Set
  A set of infrastrucute BSSs.
  Connection of APs
  Tracking of mobility
DS – Distribution System
  AP communicates with another

## Slide 25: Services
Station services:
  authentication,
  de-authentication,
  privacy,
  delivery of data
Distribution Services ( A thin layer between MAC and LLC sublayer)
  association
  disassociation
  reassociation
  distribution
  Integration
A station maintain two variables:
authentication state (=> 1)
association state (<= 1)

## Slide 26: Medium Access Control
Functionality;
Reliable data delivery
Fairly control access
Protection of data
Deals;
Noisy and unreliable medium
Frame exchange protocol - ACK
Overhead to IEEE 802.3 -
Hidden Node Problem – RTS/CTS
Participation of all stations
Reaction to every frame

## Slide 27: MAC
Retry Counters
  Short retry counter
  Long retry counter
  Lifetime timer
Basic Access Mechanism
  CSMA/CA
  Binary exponential back-off
  NAV – Network Allocation Vector
Timing Intervals: SIFS, Slot Time, PIFS, DIFS, EIFS
DCF Operation
PCF Operation

## Slide 28: PCF Operation
Poll – eliminates contention
PC – Point Coordinator
  Polling List
  Over DCF
  PIFS
CFP – Contention Free Period
  Alternate with DCF
Periodic Beacon – contains length of CFP
CF-Poll – Contention Free Poll
NAV prevents during CFP
CF-End – resets NAV

## Slide 29: Frame Types
Protocol Version
Frame Type and Sub Type
To DS and From DS
More Fragments
Retry
Power Management
More Data
WEP
Order
FC
Duration
/ID
Address
1
Address
2
Address
3
Sequence
Control
Address
4
DATA
FCS
2 2 6 6 6 2 6 0-2312 4 bytes
NAV information
Or
Short Id for PS-Poll
BSSID –BSS Identifier
TA - Transmitter
RA - Receiver
SA - Source
DA - Destination
IEEE 48 bit address
Individual/Group
Universal/Local
46 bit address
MSDU
Sequence Number
Fragment Number
CCIT CRC-32 Polynomial
Upper layer data
2048 byte max
256 upper layer header

## Slide 30: Frame Subtypes
RTS
CTS
ACK
PS-Poll
CF-End & CF-End ACK
Data
Data+CF-ACK
Data+CF-Poll
Data+CF-ACK+CF-Poll
Null Function
CF-ACK (nodata)
CF-Poll (nodata)
CF-ACK+CF+Poll
Beacon
Probe Request & Response
Authentication
Deauthentication
Association Request & Response
Reassociation Request & Response
Disassociation
Announcement Traffic Indication Message (ATIM)
CONTROL
DATA
MANAGEMENT