## Slide 1: Internet Checksum
Sum is defined in 1s complement arithmetic (must add back carries)
  And it’s the negative sum
“The checksum field is the 16 bit one's complement of the one's complement sum of all 16 bit words …” – RFC 791
Notes: Give example of 5 and -5 in 1s and 2s complement

## Slide 2: Internet Checksum (2)
Sending:
Arrange data in 16-bit words
Put zero in checksum position, add
Add any carryover back to get 16 bits
Negate (complement) to get sum
0001
f203
f4f5
f6f7
+(0000)
------
2ddf0
ddf0
+ 2
------
ddf2
220d
Notes: Work through example

## Slide 3: Internet Checksum (3)
Sending:
Arrange data in 16-bit words
Put zero in checksum position, add
Add any carryover back to get 16 bits
Negate (complement) to get sum
0001
f203
f4f5
f6f7
+(0000)
------
2ddf0
ddf0
+ 2
------
ddf2
220d

## Slide 4: Internet Checksum (4)
Receiving:
Arrange data in 16-bit words
Checksum will be non-zero, add
Add any carryover back to get 16 bits
Negate the result and check it is 0
0001
f203
f4f5
f6f7
+ 220d
------
2fffd
fffd
+ 2
------
ffff
0000
Notes: Work through example

## Slide 5: Internet Checksum (5)
Receiving:
Arrange data in 16-bit words
Checksum will be non-zero, add
Add any carryover back to get 16 bits
Negate the result and check it is 0
0001
f203
f4f5
f6f7
+ 220d
------
2fffd
fffd
+ 2
------
ffff
0000