## Slide 1
Ethernet A Case study of Physical and Data Link Layer

## Slide 2
Origin of Ethernet
Basis for the IEEE’s 802.3 specification Ethernet: It is a LAN protocol that is used in Bus and Star topologies and implements CSMA/CD as the medium access method
Found by Xerox Palo Alto Research Center (PARC) in 1975
Original designed as a 2.94 Mbps system to connect 100 computers on a 1 km cable
Ethernet developed in 1980 by three companies: Digital, Intel, Xerox (DIX) drew up a standard support 10 Mbps.
In 1985, the Computer Society of the IEEE started a project, called Project 802, to set standards to enable intercommunication among equipment from a variety of manufacturers.
Current version is called IEEE Ethernet

## Slide 3
Ethernet Basics
Topologies Linear bus, Star bus
Signaling Mainly baseband (digital)
Access method CSMA/CD
Specifications IEEE 802.3
Transfer speed 10 Mbps, 100 Mbps, 1Gbps
Cable types Coaxial cables, UTP

## Slide 4: Ethernet Standard Defines Physical Layer
802.3 standard defines both MAC and physical layer details
Metcalfe’s original
Ethernet Sketch

## Slide 5
Repeaters used to connect multiple segments
Repeater repeats bits it hears on one interface to its other interfaces: physical layer device only!

## Slide 6: IEEE Ethernet
In IEEE 802.3 Ethernet Data link layer is split into two sublayers:
  Bottom part: MAC
    The frame is called IEEE 802.3
    Handles framing, MAC addressing, Medium Access control
    Specific implementation for each LAN protocol
      Defines CSMA/CD as the access method for Ethernet LANs and Token passing method for Token Ring.
    Implemented in hardware
  Top part: LLC (Logical Link Control)
    The subframe is called IEEE 802.2
    Provides error and flow control if needed
    It makes the MAC sublayer transparent
      Allows interconnectivity between different LANs data link layers
    Used to multiplex multiple network layer protocols in the data link layer frame
    Implemented in software

## Slide 7: Ethernet Provides Unreliable, connectionless Service
  Ethernet data link layer protocol provides connectionless service to the network layer
    No handshaking between sending and receiving adapter.
  Ethernet protocol provides Unreliable service to the network layer :
    Receiving adapter doesn’t send ACK or NAK to sending adapter
    This means stream of datagrams passed to network layer can have gaps (missing data)
      Gaps will be filled if application is using reliable transport layer protocol
        Otherwise, application will see the gaps

## Slide 8
Ethernet
Frame formats. (a) DIX Ethernet , (b) IEEE 802.3.
FCS
FCS
Ethernet Frame format

## Slide 9
Figure 13.4 802.3 MAC frame

## Slide 10
Preamble:
  8 bytes with pattern 10101010 used to synchronize receiver, sender clock rates.
  In IEEE 802.3, eighth byte is start of frame (10101011)
Addresses: 6 bytes (explained latter)
Type (DIX)
  Indicates the type of the Network layer protocol being carried in the payload (data) field, mostly IP but others may be supported such as IP (0800), Novell IPX (8137) and AppleTalk (809B), ARP (0806) )
  Allow multiple network layer protocols to be supported on a single machine (multiplexing)
  Its value starts at 0600h (=1536 in decimal)
Length (IEEE 802.3): number of bytes in the data field.
  Maximum 1500 bytes (= 05DCh)
CRC: checked at receiver, if error is detected, the frame is discarded
  CRC-32
Data: carries data encapsulated from the upper-layer protocols
Pad: Zeros are added to the data field to make the minimum data length = 46 bytes
FCS: Frame Check Sequence
Ethernet Frame

## Slide 11
Ethernet address
Six bytes = 48 bits
Flat address not hierarchical
Burned into the NIC ROM
First three bytes from left specify the vendor. Cisco 00-00-0C, 3Com 02-60-8C and the last 24 bit should be created uniquely by the company
Destination Address can be:
  Unicast: second digit from left is even (one recipient)
  Multicast: Second digit from left is odd (group of stations to receive the frame – conferencing applications)
  Broadcast (ALL ones) (all stations receive the frame)
Source address is always Unicast

## Slide 13
The least significant bit of the first byte defines the type of address. If the bit is 0, the address is unicast; otherwise, it is multicast.
Note

## Slide 14
The broadcast destination address is a special case of the multicast address in which all bits are 1s.
Note

## Slide 15
Figure 13.7 Unicast and multicast addresses

## Slide 16
Ethernet Address
00 00 E2 15 1A CA
A physical address is the hardware-level address used by the Ethernet interface to communicate on the network. Every device must have a unique physical address

## Slide 17
Show how the address 47:20:1B:2E:08:EE is sent out on line.
Solution
The address is sent left-to-right, byte by byte; for each byte, it is sent right-to-left, bit by bit, as shown below:
Example 13.2

## Slide 18
Examples of Manufacturer IDs
Cisco : 00-00-0C- 3Com : 00-60-8C-
: 00-60-09- : 00-60-08-
Ethernet addresses are 48 bits long.
Ethernet addresses are governed by IEEE and are usually imprinted on Ethernet cards when the cards are manufactured.

## Slide 19
Define the type of the following destination addresses:
a. 4A:30:10:21:10:1A b. 47:20:1B:2E:08:EE
c. FF:FF:FF:FF:FF:FF
Solution
To find the type of the address, we need to look at the second hexadecimal digit from the left. If it is even, the address is unicast. If it is odd, the address is multicast. If all digits are F’s, the address is broadcast. Therefore, we have the following:
a. This is a unicast address because A in binary is 1010.
b. This is a multicast address because 7 in binary is 0111.
c. This is a broadcast address because all digits are F’s.
Example 13.1

## Slide 20
Frame length:
Minimum: 64 bytes (512 bits) Maximum: 1518 bytes (12,144 bits)
Note

## Slide 21
Figure 13.3 Ethernet evolution through four generations

## Slide 22
Baseband Transmission
  Entire channel is used to transmit a single digital signal
  Complete bandwidth of the cable is used by a single signal
  The transmission distance is shorter
  The electrical interference is lower
Broadband Transmission
  Use analog signaling and a range of frequencies
  Continuous signals flow in the form of waves
  Support multiple analog transmission (channels)
Modem
Broadband Transmission
Network Card
Baseband Transmission

## Slide 23
Categories of traditional Ethernet
<data rate><Signaling method><Max segment length or cable type>

## Slide 24: IEEE 802.3 Cable Types
Name | Cable Max. | Max Cable Segment Length | Nodes /segment
10Base5 | thick coax | 500 meters | 100
10Base2 | thin coax | 185 meters | 30
10BaseT | twisted pair | 100 meters | 1
10BaseF | Fiber Optic | 2Km | 1
Toplogy
Bus
Bus
Star
Star

## Slide 25
Figure 13.10 10Base5 implementation

## Slide 26
Connection of stations to the medium using 10Base2

## Slide 27
10BaseT
• Uses twisted pair Cat3 cable
Star-wire topology
• A hub functions as a repeater with additional functions
• Fewer cable problems, easier to troubleshoot than coax
• Cable length at most 100 meters

## Slide 28
Figure 13.12 10Base-T implementation

## Slide 29
Figure 13.13 10Base-F implementation

## Slide 30: 13.4 Fast Ethernet
100 Mbps transmission rate
same frame format, media access, and collision detection rules as 10 Mbps Ethernet
can combine 10 Mbps Ethernet and Fast Ethernet on same network using a switch
media: twisted pair (CAT 5) or fiber optic cable (no coax)
Star-wire topology
  Similar to 10BASE-T
CAT 3
CAT 5

## Slide 31
Figure 13.19 Fast Ethernet topology

## Slide 32
Figure 13.20 Fast Ethernet implementations

## Slide 33
Full Duplex Operation
Traditional Ethernet is half duplex
  Either transmit or receive but not both simultaneously
With full-duplex, station can transmit and receive data simultaneously
With full duplex, Throughput (actual transmission rate) is doubled.
  10-Mbps Ethernet in full-duplex mode, theoretical transfer rate becomes 20 Mbps
  100-Mbps Ethernet in full-duplex mode, theoretical transfer rate becomes 200 Mbps
Changes that should be made with any computer in order to operate in Full-Duplex Mode
  Attached stations must have full-duplex NIC cards
  Must use two pairs of wire one pair for transmitting from host to switch (inbound) and the other pair for transmitting from switch to host (outbound)
  Must use a switch as a central device not a hub
  Devices must be connected point-to-point (dedicated) to the switch
  Each station constitutes separate collision domain
    CSMA/CD algorithm no longer needed (no collision)
    No limit on the segment length
    Same 802.3 MAC frame format used

## Slide 34
Figure 13.18 Full-duplex switched Ethernet

## Slide 35
Figure 13.17 Switched Ethernet

## Slide 36: 13.5 Gigabit Ethernet
Speed 1Gpbs
Minimum frame length is 512 bytes
Operates in full/half duplex modes mostly full duplex
Speed 1Gpbs
Minimum frame length is 512 bytes
Operates in full/half duplex modes mostly full duplex

## Slide 37
In the full-duplex mode of Gigabit Ethernet, there is no collision;
the maximum length of the cable is determined by the signal attenuation in the cable.
Note

## Slide 38
Figure 13.22 Topologies of Gigabit Ethernet

## Slide 39
Figure 13.23 Gigabit Ethernet implementations

## Slide 40
10Gbps Ethernet
Maximum link distances cover 300 m to 40 km
Full-duplex mode only
No CSMA/CD
Uses optical fiber only

## Slide 41: Ethernet’s MAC Algorithm(Access Method - CSMA/CD )
In Aloha, decisions to transmit are made without paying attention to what other nodes might be doing
Ethernet uses CSMA/CD – listens to line before/during sending
If line is idle (no carrier sensed)
  send packet immediately
  upper bound message size of 1500 bytes
  must wait 9.6us between back-to-back frames
If line is busy (carrier sensed)
  wait until idle and transmit packet immediately
    called 1-persistent sending
If collision detected
  Stop sending and jam signal
  Try again later

## Slide 42: Collisions
Collisions are caused when two adaptors transmit at the same
time (adaptors sense collision based on voltage differences)
  Both found line to be idle
  Both had been waiting to for a busy line to become idle
A
B
A
B
A starts at
time 0
Message almost
there at time T when
B starts – collision!
How can we be sure A knows about the collision?

## Slide 43: Collision Detection
How can A know that a collision has taken place?
  There must be a mechanism to insure retransmission on collision
  A’s message reaches B at time T
  B’s message reaches A at time 2T
  So, A must still be transmitting at 2T
IEEE 802.3 specifies max value of 2T to be 51.2us
  This relates to maximum distance of 2500m between hosts
  At 10Mbps it takes 0.1us to transmit one bit so 512 bits (64B) take 51.2us to send
  So, Ethernet frames must be at least 64B long
    14B header, 46B data, 4B CRC
    Padding is used if data is less than 46B
Send jamming signal after collision is detected to insure all hosts see collision
  48 bit signal

## Slide 44: Collision Detection contd.
A
B
A
B
A
B
time = 0
time = T
time = 2T

## Slide 45: Exponential Backoff
If a collision is detected, delay and try again
Delay time is selected using binary exponential backoff
  1st time: choose K from {0,1} then delay = K * 51.2us
  2nd time: choose K from {0,1,2,3} then
  delay = K * 51.2us
  nth time: delay = K x 51.2us, for K=0..2n – 1
    Note max value for k = 1023
  give up after several tries (usually 16)
    Report transmit error to host

## Slide 46: Exponential Backoff
When a collision first occurs, send a “Jamming signal” to prevent further data being sent.
Resend a frame after either 0 seconds or 51.2μs, chosen at random.
If that fails, resend the frame after either 0s, 51.2μs, 102.4μs, or 153.6μs.
If that still doesn't work, resend the frame after k · 51.2μs, where k is a random integer between 0 and 23 − 1.
In general, after the cth failed attempt, resend the frame after k · 51.2μs, where k is a random integer between 0 and 2c − 1.

## Slide 47
Exponential Backoff Algorithm used in CSMA/CD

## Slide 48: MAC Algorithm from the Receiver Side
Senders handle all access control
Receivers simply read frames with acceptable address
  Address to host
  Address to broadcast
  Address to multicast to which host belongs

## Slide 49
CSMA/CD ― Design Considerations
More computers on the LAN, higher chance of collisions
Retransmission may result in collision again and cause further delay
As the result, the network becomes standstill
Hence, Ethernet is suitable for low traffic networks