## Slide 1: William Stallings Data and Computer Communications 7th Edition
Chapter 17 Wireless LANs

## Slide 2: Overview
A wireless LAN uses wireless transmission medium
Used to have high prices, low data rates, occupational safety concerns, and licensing requirements
Problems have been addressed
Popularity of wireless LANs has grown rapidly

## Slide 3: Applications - LAN Extension
Saves installation of LAN cabling
Eases relocation and other modifications to network structure
However, increasing reliance on twisted pair cabling for LANs
  Most older buildings already wired with Cat 3 cable
  Newer buildings are prewired with Cat 5
Wireless LAN to replace wired LANs has not happened
In some environments, role for the wireless LAN
  Buildings with large open areas
    Manufacturing plants, stock exchange trading floors, warehouses
    Historical buildings
    Small offices where wired LANs not economical
May also have wired LAN
  Servers and stationary workstations

## Slide 4: Single Cell Wireless LAN Configuration

## Slide 5: Multi-Cell Wireless LAN Configuration

## Slide 6: Applications – Cross-Building Interconnect
Connect LANs in nearby buildings
Point-to-point wireless link
Connect bridges or routers
Not a LAN per se
  Usual to include this application under heading of wireless LAN

## Slide 7: Applications - Nomadic Access
Link between LAN hub and mobile data terminal
  Laptop or notepad computer
  Enable employee returning from trip to transfer data from portable computer to server
Also useful in extended environment such as campus or cluster of buildings
  Users move around with portable computers
  May wish access to servers on wired LAN

## Slide 8: Infrastructure Wireless LAN

## Slide 9: Applications – Ad Hoc Networking
Peer-to-peer network
Set up temporarily to meet some immediate need
E.g. group of employees, each with laptop or palmtop, in business or classroom meeting
Network for duration of meeting

## Slide 10: Add Hoc LAN

## Slide 11: Wireless LAN Requirements
Same as any LAN
  High capacity, short distances, full connectivity, broadcast capability
Throughput: efficient use wireless medium
Number of nodes:Hundreds of nodes across multiple cells
Connection to backbone LAN: Use control modules to connect to both types of LANs
Service area: 100 to 300 m
Low power consumption:Need long battery life on mobile stations
  Mustn't require nodes to monitor access points or frequent handshakes
Transmission robustness and security:Interference prone and easily eavesdropped
Collocated network operation:Two or more wireless LANs in same area
License-free operation
Handoff/roaming: Move from one cell to another
Dynamic configuration: Addition, deletion, and relocation of end systems without disruption to users

## Slide 12: Technology
Infrared (IR) LANs: Individual cell of IR LAN limited to single room
  IR light does not penetrate opaque walls
Spread spectrum LANs: Mostly operate in ISM (industrial, scientific, and medical) bands
  No Federal Communications Commission (FCC) licensing is required in USA
Narrowband microwave: Microwave frequencies but not use spread spectrum
  Some require FCC licensing

## Slide 13: Infrared LANs Strengths and Weaknesses
Spectrum virtually unlimited
  Infrared spectrum is unregulated worldwide
  Extremely high data rates
Infrared shares some properties of visible light
  Diffusely reflected by light-colored objects
    Use ceiling reflection to cover entire room
  Does not penetrate walls or other opaque objects
    More easily secured against eavesdropping than microwave
    Separate installation in every room without interference
Inexpensive and simple
  Uses intensity modulation, so receivers need to detect only amplitude
Background radiation
  Sunlight, indoor lighting
  Noise, requiring higher power and limiting range
  Power limited by concerns of eye safety and power consumption

## Slide 14: Infrared LANs Transmission Techniques
Directed-beam IR
  Point-to-point links
  Range depends on power and focusing
    Can be kilometers
    Used for building interconnect within line of sight
  Indoor use to set up token ring LAN
  IR transceivers positioned so that data circulate in ring
Omnidirectional
  Single base station within line of sight of all other stations
    Typically, mounted on ceiling
  Acts as a multiport repeater
  Other transceivers use directional beam aimed at ceiling unit
Diffused configuration
  Transmitters are focused and aimed at diffusely reflecting ceiling

## Slide 15: Spread Spectrum LANs Hub Configuration
Usually use multiple-cell arrangement
Adjacent cells use different center frequencies
Hub is typically mounted on ceiling
  Connected to wired LAN
  Connect to stations attached to wired LAN and in other cells
  May also control access
    IEEE 802.11 point coordination function
  May also act as multiport repeater
    Stations transmit to hub and receive from hub
  Stations may broadcast using an omnidirectional antenna
    Logical bus configuration
Hub may do automatic handoff
  Weakening signal, hand off

## Slide 16: Spread Spectrum LANs Peer-to-Peer Configuration
No hub
MAC algorithm such as CSMA used to control access
Ad hoc LANs

## Slide 17: Spread Spectrum LANs Transmission Issues
Licensing regulations differ from one country to another
USA FCC authorized two unlicensed applications within the ISM band:
  Spread spectrum - up to 1 watt
  Very low power systems- up to 0.5 watts
  902 - 928 MHz (915-MHz band)
  2.4 - 2.4835 GHz (2.4-GHz band)
  5.725 - 5.825 GHz (5.8-GHz band)
  2.4 GHz also in Europe and Japan
  Higher frequency means higher potential bandwidth
Interference
  Devices at around 900 MHz, including cordless telephones, wireless microphones, and amateur radio
  Fewer devices at 2.4 GHz; microwave oven
  Little competition at 5.8 GHz
    Higher frequency band, more expensive equipment

## Slide 18: Narrow Band Microwave LANs
Just wide enough to accommodate signal
Until recently, all products used licensed band
At least one vendor has produced LAN product in ISM band

## Slide 19: Licensed Narrowband RF
Microwave frequencies usable for voice, data, and video licensed within specific geographic areas to avoid interference
  Radium 28 km
  Can contain five licenses
  Each covering two frequencies
  Motorola holds 600 licenses (1200 frequencies) in the 18-GHz range
  Cover all metropolitan areas with populations of 30,000 or more in USA
Use of cell configuration
Adjacent cells use nonoverlapping frequency bands
Motorola controls frequency band
  Can assure nearby independent LANs do not interfere
All transmissions are encrypted
Licensed narrowband LAN guarantees interference-free communication
License holder has legal right tointerference-free data channel

## Slide 20: Unlicensed Narrowband RF
1995, RadioLAN introduced narrowband wireless LAN using unlicensed ISM spectrum
  Used for narrowband transmission at low power
    0.5 watts or less
  Operates at 10 Mbps
  5.8-GHz band
  50 m in semiopen office and 100 m in open office
Peer-to-peer configuration
Elects one node as dynamic master
  Based on location, interference, and signal strength
Master can change automatically as conditions change
Includes dynamic relay function
Stations can act as repeater to move data between stations that are out of range of each other

## Slide 21: IEEE 802.11 - BSS
MAC protocol and physical medium specification for wireless LANs
Smallest building block is basic service set (BSS)
  Number of stations
  Same MAC protocol
  Competing for access to same shared wireless medium
May be isolated or connect to backbone distribution system (DS) through access point (AP)
  AP functions as bridge
MAC protocol may be distributed or controlled by central coordination function in AP
BSS generally corresponds to cell
DS can be switch, wired network, or wireless network

## Slide 22: BSS Configuration
Simplest: each station belongs to single BSS
  Within range only of other stations within BSS
Can have two BSSs overlap
  Station could participate in more than one BSS
Association between station and BSS dynamic
  Stations may turn off, come within range, and go out of range

## Slide 23: Extended Service Set (ESS)
Two or more BSS interconnected by DS
  Typically, DS is wired backbone but can be any network
Appears as single logical LAN to LLC

## Slide 24: Access Point (AP)
Logic within station that provides access to DS
  Provides DS services in addition to acting as station
To integrate IEEE 802.11 architecture with wired LAN, portal used
Portal logic implemented in device that is part of wired LAN and attached to DS
  E.g. Bridge or router

## Slide 25: IEEE 802.11 Architecture

## Slide 26: Services
Service | Provider | Category
Association | Distribution system | MSDU delivery
Authentication | Station | LAN access and security
Deauthentication | Station | LAN access and security
Dissassociation | Distribution system | MSDU delivery
Distribution | Distribution system | MSDU delivery
Integration | Distribution system | MSDU delivery
MSDU delivery | Station | MSDU delivery
Privacy | Station | LAN access and security
Reassocation | Distribution system | MSDU delivery

## Slide 27: Categorizing Services
Station services implemented in every 802.11 station
  Including AP stations
Distribution services provided between BSSs
  May be implemented in AP or special-purpose device
Three services used to control access and confidentiality
Six services used to support delivery of MAC service data units (MSDUs) between stations
  Block of data passed down from MAC user to MAC layer
  Typically LLC PDU
  If MSDU too large for MAC frame, fragment and transmit in series of frames (see later)

## Slide 28: Distribution of Messages Within a DS
Distribution is primary service used by stations to exchange MAC frames when frame must traverse DS
  From station in one BSS to station in another BSS
  Transport of message through DS is beyond scope of 802.11
  If stations within same BSS, distribution service logically goes through single AP of that BSS
Integration service enables transfer of data between station on 802.11 LAN and one on an integrated 802.x LAN
  Integrated refers to wired LAN physically connected to DS
    Stations may be logically connected to 802.11 LAN via integration service
  Integration service takes care of address translation and media conversion

## Slide 29: Association Related Services
Purpose of MAC layer transfer MSDUs between MAC entities
Fulfilled by distribution service (DS)
DS requires information about stations within ESS
  Provided by association-related services
  Station must be associated before communicating
Three transition types of based on mobility
  No transition: Stationary or moves within range of single BSS
  BSS transition: From one BSS to another within same ESS
    Requires addressing capability be able to recognize new location
ESS transition: From BSS in one ESS to BSS in another ESS
  Only supported in sense that the station can move
  Maintenance of upper-layer connections not guaranteed
  Disruption of service likely

## Slide 30: Station Location
DS needs to know where destination station is
  Identity of AP to which message should be delivered
  Station must maintain association with AP within current BSS
Three services relate to this requirement:
  Association: Establishes initial association between station and AP
    To make identity and address known
    Station must establish association with AP within particular BSS
    AP then communicates information to other APs within ESS
  Reassociation: Transfer established association to another AP
    Allows station to move from one BSS to another
  Disassociation: From either station or AP that association is terminated
  Given before station leaves ESS or shuts
    MAC management facility protects itself against stations that disappear without notification

## Slide 31: Access and Privacy Services - Authentication
On wireless LAN, any station within radio range other devices can transmit
Any station within radio range can receive
Authentication: Used to establish identity of stations to each other
  Wired LANs assume access to physical connection conveys authority to connect to LAN
  Not valid assumption for wireless LANs
    Connectivity achieved by having properly tuned antenna
  Authentication service used to establish station identity
  802.11 supports several authentication schemes
    Allows expansion of these schemes
  Does not mandate any particular scheme
  Range from relatively insecure handshaking to public-key encryption schemes
  802.11 requires mutually acceptable, successful authentication before association

## Slide 32: Access and Privacy Services - Deauthentication and Privacy
Deauthentication: Invoked whenever an existing authentication is to be terminated
Privacy: Used to prevent messages being read by others
802.11 provides for optional use of encryption

## Slide 33: Medium Access Control
MAC layer covers three functional areas
Reliable data delivery
Access control
Security
  Beyond our scope

## Slide 34: Reliable Data Delivery
802.11 physical and MAC layers subject to unreliability
Noise, interference, and other propagation effects result in loss of frames
Even with error-correction codes, frames may not successfully be received
Can be dealt with at a higher layer, such as TCP
  However, retransmission timers at higher layers typically order of seconds
  More efficient to deal with errors at the MAC level
802.11 includes frame exchange protocol
  Station receiving frame returns acknowledgment (ACK) frame
  Exchange treated as atomic unit
    Not interrupted by any other station
  If noACK within short period of time, retransmit

## Slide 35: Four Frame Exchange
Basic data transfer involves exchange of two frames
To further enhance reliability, four-frame exchange may be used
  Source issues a Request to Send (RTS) frame to destination
  Destination responds with Clear to Send (CTS)
  After receiving CTS, source transmits data
  Destination responds with ACK
RTS alerts all stations within range of source that exchange is under way
CTS alerts all stations within range of destination
Stations refrain from transmission to avoid collision
RTS/CTS exchange is required function of MAC but may be disabled

## Slide 36: Media Access Control
Distributed wireless foundation MAC (DWFMAC)
  Distributed access control mechanism
  Optional centralized control on top
Lower sublayer is distributed coordination function (DCF)
  Contention algorithm to provide access to all traffic
  Asynchronous traffic
Point coordination function (PCF)
  Centralized MAC algorithm
  Contention free
  Built on top of DCF

## Slide 37: IEEE 802.11 Protocol Architecture

## Slide 38: Distributed Coordination Function
DCF sublayer uses CSMA
If station has frame to transmit, it listens to medium
If medium idle, station may transmit
Otherwise must wait until current transmission complete
No collision detection
  Not practical on wireless network
  Dynamic range of signals very large
  Transmitting station cannot distinguish incoming weak signals from noise and effects of own transmission
DCF includes delays
  Amounts to priority scheme
    Interframe space

## Slide 39: Interframe Space
Single delay known as interframe space (IFS)
Using IFS, rules for CSMA:
Station with frame senses medium
  If idle, wait to see if remains idle for one IFS. If so, may transmit immediately
If busy (either initially or becomes busy during IFS) station defers transmission
  Continue to monitor until current transmission is over
Once current transmission over, delay another IFS
  If remains idle, back off random time and again sense
  If medium still idle, station may transmit
  During backoff time, if becomes busy, backoff timer is halted and resumes when medium becomes idle
To ensure stability, binary exponential backoff used

## Slide 40: IEEE 802.11 Medium Access Control Logic

## Slide 41: Priority
Use three values for IFS
SIFS (short IFS):
  Shortest IFS
  For all immediate response actions (see later)
PIFS (point coordination function IFS):
  Midlength IFS
  Used by the centralized controller in PCF scheme when issuing polls
DIFS (distributed coordination function IFS):
  Longest IFS
  Used as minimum delay for asynchronous frames contending for access

## Slide 42: SIFS Use - ACK
Station using SIFS to determine transmission opportunity has highest priority
  In preference to station waiting PIFS or DIFS time
SIFS used in following circumstances:
Acknowledgment (ACK): Station responds with ACK after waiting SIFS gap
  No collision detection so likelihood of collisions greater than CSMA/CD
    MAC-level ACK gives efficient collision recovery
  SIFS provide efficient delivery of multiple frame LLC PDU
    Station with multiframe LLC PDU to transmit sends out MAC frames one at a time
    Each frame acknowledged after SIFS by recipient
    When source receives ACK, immediately (after SIFS) sends next frame in sequence
    Once station has contended for channel, it maintains control of all fragments sent

## Slide 43: SIFS Use – CTS
Clear to Send (CTS): Station can ensure data frame will get through by issuing RTS
  Destination station should immediately respond with CTS if ready to receive
  All other stations hear RTS and defer
Poll response: See Point coordination Function (PCF)

## Slide 44: PIFS and DIFS
PIFS used by centralized controller
  Issuing polls
  Takes precedence over normal contention traffic
  Frames using SIFS have precedence over PCF poll
DIFS used for all ordinary asynchronous traffic

## Slide 45: IEEE 802.11 MAC Timing Basic Access Method

## Slide 46: Point Coordination Function (PCF)
Alternative access method implemented on top of DCF
Polling by centralized polling master (point coordinator)
Uses PIFS when issuing polls
  PIFS smaller than DIFS
  Can seize medium and lock out all asynchronous traffic while it issues polls and receives responses
E.g. wireless network configured so number of stations with time-sensitive traffic controlled by point coordinator
  Remaining traffic contends for access using CSMA
Point coordinator polls in round-robin to stations configured for polling
When poll issued, polled station may respond using SIFS
If point coordinator receives response, it issues another poll using PIFS
If no response during expected turnaround time, coordinator issues poll

## Slide 47: Superframe
Point coordinator would lock out asynchronous traffic by issuing polls
Superframe interval defined
  During first part of superframe interval, point coordinator polls round-robin to all stations configured for polling
  Point coordinator then idles for remainder of superframe
  Allowing contention period for asynchronous access
At beginning of superframe, point coordinator may seize control and issue polls for given period
  Time varies because of variable frame size issued by responding stations
Rest of superframe available for contention-based access
At end of superframe interval, point coordinator contends for access using PIFS
If idle, point coordinator gains immediate access
  Full superframe period follows
  If busy, point coordinator must wait for idle to gain access
  Results in foreshortened superframe period for next cycle

## Slide 48: IEEE 802.11 MAC Timing PCF Superframe Construction

## Slide 49: IEEE 802.11 MAC Frame Format

## Slide 50: MAC Frame Fields (1)
Frame Control:
  Type of frame
  Control, management, or data
  Provides control information
    Includes whether frame is to or from DS, fragmentation information, and privacy information
Duration/Connection ID:
  If used as duration field, indicates time (in s) channel will be allocated for successful transmission of MAC frame
  In some control frames, contains association or connection identifier
Addresses:
  Number and meaning of address fields depend on context
  Types include source, destination, transmitting station, and receiving station

## Slide 51: MAC Frame Fields (2)
Sequence Control:
  4-bit fragment number subfield
    For fragmentation and reassembly
  12-bit sequence number
  Number frames between given transmitter and receiver
Frame Body:
  MSDU (or a fragment of)
    LLC PDU or MAC control information
Frame Check Sequence:
  32-bit cyclic redundancy check

## Slide 52: Control Frames
Assist in reliable data delivery
Power Save-Poll (PS-Poll)
  Sent by any station to station that includes AP
  Request AP transmit frame buffered for this station while station in power-saving mode
Request to Send (RTS)
  First frame in four-way frame exchange
Clear to Send (CTS)
  Second frame in four-way exchange
Acknowledgment (ACK)
Contention-Free (CF)-end
  Announces end of contention-free period part of PCF
CF-End + CF-Ack:
  Acknowledges CF-end
  Ends contention-free period and releases stations from associated restrictions

## Slide 53: Data Frames – Data Carrying
Eight data frame subtypes, in two groups
First four carry upper-level data from source station to destination station
Data
  Simplest data frame
  May be used in contention or contention-free period
Data + CF-Ack
  Only sent during contention-free period
  Carries data and acknowledges previously received data
Data + CF-Poll
  Used by point coordinator to deliver data
  Also to request station send data frame it may have buffered
Data + CF-Ack + CF-Poll
  Combines Data + CF-Ack and Data + CF-Poll

## Slide 54: Data Frames – Not Data Carrying
Remaining four data frames do not carry user data
Null Function
  Carries no data, polls, or acknowledgments
  Carries power management bit in frame control field to AP
  Indicates station is changing to low-power state
Other three frames (CF-Ack, CF-Poll, CF-Ack + CF-Poll) same as corresponding frame in preceding list (Data + CF-Ack, Data + CF-Poll, Data + CF-Ack + CF-Poll) but without data

## Slide 55: Management Frames
Used to manage communications between stations and Aps
E.g. management of associations
  Requests, response, reassociation, dissociation, and authentication

## Slide 56: 802.11 Physical Layer
Issued in four stages
First part in 1997
  IEEE 802.11
  Includes MAC layer and three physical layer specifications
  Two in 2.4-GHz band and one infrared
  All operating at 1 and 2 Mbps
Two additional parts in 1999
  IEEE 802.11a
    5-GHz band up to 54 Mbps
  IEEE 802.11b
    2.4-GHz band at 5.5 and 11 Mbps
Most recent in 2002
  IEEE 802.g extends IEEE 802.11b to higher data rates

## Slide 57: Original 802.11 Physical Layer - DSSS
Three physical media
Direct-sequence spread spectrum
  2.4 GHz ISM band at 1 Mbps and 2 Mbps
  Up to seven channels, each 1 Mbps or 2 Mbps, can be used
  Depends on bandwidth allocated by various national regulations
    13 in most European countries
    One in Japan
  Each channel bandwidth 5 MHz
  Encoding scheme DBPSK for 1-Mbps and DQPSK for 2-Mbps

## Slide 58: Original 802.11 Physical Layer - FHSS
Frequency-hopping spread spectrum
  2.4 GHz ISM band at 1 Mbps and 2 Mbps
  Uses multiple channels
  Signal hopping from one channel to another based on a pseudonoise sequence
  1-MHz channels are used
  23 channels in Japan
  70 in USA
Hopping scheme adjustable
  E.g. Minimum hop rate forUSA is 2.5 hops per second
  Minimum hop distance 6 MHz in North America and most of Europe and 5 MHz in Japan
Two-level Gaussian FSK modulation for 1-Mbps
  Bits encoded as deviations from current carrier frequency
For 2 Mbps, four-level GFSK used
  Four different deviations from center frequency define four 2-bit combinations

## Slide 59: Original 802.11 Physical Layer – Infrared
Omnidirectional
Range up to 20 m
1 Mbps used 16-PPM (pulse position modulation)
  Each group of 4 data bits mapped into one of 16-PPM symbols
  Each symbol a string of 16 bits
  Each 16-bit string consists of fifteen 0s and one binary 1
For 2-Mbps, each group of 2 data bits is mapped into one of four 4-bit sequences
  Each sequence consists of three 0s and one binary 1
  Intensity modulation
    Presence of signal corresponds to 1

## Slide 60: 802.11a
5-GHz band
Uses orthogonal frequency division multiplexing (OFDM)
  Not spread spectrum
Also called multicarrier modulation
Multiple carrier signals at different frequencies
Some bits on each channel
  Similar to FDM but all subchannels dedicated to single source
Data rates 6, 9, 12, 18, 24, 36, 48, and 54 Mbps
Up to 52 subcarriers modulated using BPSK, QPSK, 16-QAM, or 64-QAM
  Depending on rate
  Subcarrier frequency spacing 0.3125 MHz
  Convolutional code at rate of 1/2, 2/3, or 3/4 provides forward error correction

## Slide 61: 802.11b
Extension of 802.11 DS-SS scheme
5.5 and 11 Mbps
Chipping rate 11 MHz
  Same as original DS-SS scheme
  Same occupied bandwidth
  Complementary code keying (CCK) modulation to achieve higher data rate in same bandwidth at same chipping rate
  CCK modulation complex
    Overview on next slide
  Input data treated in blocks of 8 bits at 1.375 MHz
    8 bits/symbol  1.375 MHz = 11 Mbps
    Six of these bits mapped into one of 64 code sequences
    Output of mapping, plus two additional bits, forms input to QPSK modulator

## Slide 62: 11-Mbps CCK Modulation Scheme

## Slide 63: 802.11g
Higher-speed extension to 802.11b
Combines physical layer encoding techniques used in 802.11a and 802.11b to provide service at a variety of data rates

## Slide 64: Required Reading
Stallings chapter 17
Web sites on 802.11