## Slide 2: What is bluetooth?
Bluetooth wireless technology is an open specification for a low-cost, low-power, short-range radio technology for ad-hoc wireless communication of voice and data anywhere in the world.
It is a cable replacement technology.
Wireless communication between various devices within a small area.
Used to swap data and synchronize between various devices

## Slide 3: Introduction
1994 Ericsson gets interested in wireless connections from mobile telephones to other devices like PDAs and accessories like Headsets
Forming the SIG (SpecialInterestGroup) with 4 other members (IBM, Intel, Nokia, Toshiba) in order to develop a wireless standard for communication between mobile devices

## Slide 4: Introdution
Today over 2000 members
2 main priorities:
  Cheap
  Lower energy consumption
IEEE 802.15 committee standardizes the physical and link layer
SIG still enhances Bluetooth
  two versions in future possible
  (SIG vs IEEE)

## Slide 5: Overview
Originally conceived as a cable replacement technology
Other usage models began to develop:
  Personal Area Network (PAN)
  Ad-hoc networks
  Data/voice access points
  Wireless telematics

## Slide 6: Overview
Advantages
  Bluetooth: interoperable
  Infrared Data Association IrDA: line of sight needed, point-to-point
  WLAN: higher power consumption
Disadvantages
  Bluetooth: only up to 1 Mbps
  IrDA: much cheaper, faster (up to 16 Mbps)
  WLAN: faster (up to 11 Mbps)
WLAN and Bluetooth interfere each other (both are using the ISM band)

## Slide 7: Frequency Band
Diff Frequency ranges for diff countries.
Europe & USA-2400-2483.5 MHz.
Japan-2471-2497 MHz.
Spain-2445-2475 MHz.
France-2445-2483.5 MHz.
SIG Working towards harmonization of frequency.

## Slide 8: How it works
Bluetooth is based on low cost, short-ranged radio link, operates in Radio band of 2.4GHz , and provides a range of 10 meters.
Connections can be point-to-point or multipoint.
Devices connected to each other, they form a personal area network (PAN) called the Pico net.
Each Pico net can have a master, and up to 7 active and 255 parked slaves.
Different Pico nets are connected using a common device and such networks are called scatter net

## Slide 12: Ad-hoc-networking
piconet
  decentral, one master up to 7 slaves
  up to 255 parked slaves
  point to point or point to multipoint conn
  unique bluetooth device address
scatternet
  overlapping of two piconets, up to 10
  different hopping sequences
  peer to peer (P2P) network

## Slide 13: Ad-hoc-networking
a: piconet with a single slave
b: piconet with a multi slave
c: scatternet

## Slide 14: Bluetooth Protocol Stack
RF
Baseband
Link Manager
L2CAP
RFCOMM/SDP
Applications
Link Controller
Host Controller Interface
PHY
Data Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application
OSI/ISO

## Slide 15: Specifications & Layers
specification protocol stack

## Slide 16: Specifications & Layers

## Slide 17: Layers
Bluetooth Radio
Baseband
LMP (Link Manager Protocol)
HCI (Host Controller Interface)
L2CAP (Logical Link Control and Adaptation Protocol)
RFCOMM (Radio Frequency Communication)
SDP (Service Discovery Protocol)

## Slide 18: Bluetooth Radio
the lowest defined layer of the Bluetooth specification
operating in the 2,4 GHz ISM Band
accomplishes spectrum spreading by frequency hopping (FHSS) from 2.402 GHz to 2.480 GHz

## Slide 19: Bluetooth Radio
3 different power classes
  Power Class1: long range (100m,100mW)
  Power Class2: mid range (10m,1-2,5mW)
  Power Class3: short range (0.1-10m,1mW)
signal strength adjustment

## Slide 20: Baseband
the physical layer of the Bluetooth that provides
  Error correction
  Flow control
  Hopping sequence
  Security
hopping through 79 channels
data is divided in packets
  access code: e.g. timing synchronization
  header: e.g. packet numbering, flow control, slave address
  payload: voice, data or both

## Slide 21: Baseband
Connection Modes
It describes the set of rules by which all bluetooth devices must abide in order to establish a link a communicate with one another
  STANDBY : not connected in a piconet
  ACTIVE : active participation on the channel
  Power Saving Modes
    SNIFF : slave listens to the channel at a reduced rate (decreasing of duty cycle ) least power efficient
    HOLD : data transfer is held for a specific time period, medium power efficient
    PARK : synchronized to the piconet but does not participate in traffic

## Slide 22: Baseband
Security Modes
  non-secure
  encryption enforced by application layer
  encryption enforced by link layer
  For devices
    trusted device
    untrusted device
  For services
    require authorization and authentication
    require authentication
    open to all devices

## Slide 23: Audio
two codecs: PCM and CVSD
both at 64kbit/s
synchronous connection oriented(SCO) links
time-critical
no retransmission
errors appear as background noise

## Slide 24: LMP (Link Manager Protocol)
provides authentication, link setup and link configuration including power surveillance
takes place as a service provider
communication with LM PDUs (protocol data units)

## Slide 25: HCI (Host Controller Interface)
provides a command interface to baseband controller and link manager
also to hardware status, control and event register
Bluetooth defined Host Controller Transport Layers:
  UART (HCI over serial interface)
  RS232(HCI over serial interface)
  USB(HCI over USB interface e.g. USB dongle)

## Slide 26: L2CAP (Logical Link Control and Adaptation Protocol)
provides a connection-oriented and connectionless service to upper layer
protocols with quality-of-service functions using multiplexing, segmentation and reassembly
two link types defined in Baseband layer:
  1. SCO (synchronous connection-oriented)
  2. ACL (asynchronous connection-less)
BUT ONLY ACL is supported by L2CAP
(SCO not planned)

## Slide 27: RFCOMM (Radio Frequency Communication)
Provides emulation of serial ports
Supports up to 60 simultaneous connections
Differentiates between two device types:
  Type 1: communication end points (e.g. printer or headsets)
  Type 2: devices which are part of communication (e.g. modems)
But in the protocol itself no distinction is made, some information is for type 1 other for type 2

## Slide 28: SDP (Service Discovery Protocol)
discovers which services are available
identifies the characteristics of the services
uses a request/response model where each transaction consists of one request protocol data unit (PDU) and one response PDU
SDP is used with L2CAP
is optimized for the dynamic nature of bluetooth
SDP does not define methods for accessing services

## Slide 29: SDP (Service Discovery Protocol)

## Slide 30
Wireless Application Protocol (WAP)
Wide Area Ethernet (WAE)
TCS-BIN Telephony Control Specification—Binary
AT commands --modem commands are called AT commands.
Many of the commands that are used to control wired dial-up modems, such as ATD (Dial), ATA (Answer), ATH (Hook control) and ATO (Return to online data state)