## Slide 1: Network Models

## Slide 2: LAYERED TASKS
We use the concept of layers in our daily life. As an example, let us consider two friends who communicate through postal mail. The process of sending a letter to a friend would be complex if there were no services available from the post office.

## Slide 3: Layered Tasks, Example

## Slide 4: THE OSI MODEL
Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on international standards. An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model. It was first introduced in the late 1970s.
Note:
  ISO is the organization.
  OSI is the model.

## Slide 5: Seven layers of the OSI model

## Slide 6
All people seem to need data processing.“
All = Application Layer
People = Presentation Layer
Seem = Session Layer
To = Transport Layer
Need =
Network Layer
Data = Data Link Layer
Processing = Physical Layer

## Slide 7
PLEASE DO NOT TOUCH STEVE’ S PET ALLIGATOR
OSI Layers Mnemonic
Layer 1: Physical = Please.
Layer 2: Data Link = Do.
Layer 3: Network = Not.
Layer 4: Transport = Touch.
Layer 5: Session = Steve's.
Layer 6: Presentation = Pet.
Layer 7: Application = Alligator

## Slide 8: Interfaces b/w Layers

## Slide 9: Exchange using the OSI Model

## Slide 10: LAYERS IN THE OSI MODEL
Physical Layer
Data Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer

## Slide 11: Physical Layer
The physical layer is responsible for movements of individual bits from one hop (node) to the next.
  Physical characteristics of interface and medium: pin assignment, connector, cables
  Representation of bits: encoding
  Data rate
  Synchronization of bits
  Line configuration: point-to-point, multipoint
  Physical topology
  Transmission mode: simplex, half-duplex, full-duplex

## Slide 12: Data Link Layer
The data link layer is responsible for moving frames from one hop (node) to the next.
  Framing
  Physical addressing
  Flow control
  Error control
  Access control

## Slide 13: Hop-to-hop Delivery

## Slide 14: Network Layer
The network layer is responsible for the delivery of individual packets from the source host to the destination host.
  Logical addressing
  Routing

## Slide 15: Source-to-destination delivery

## Slide 16: Transport layer
The transport layer is responsible for the delivery of a message from one process to another.
  Service-point addressing
  Segmentation and reassembly
  Connection control
  Flow control
  Error control

## Slide 17: Segmentation and Reassembly

## Slide 18: Reliable process-to-process delivery of a message

## Slide 19: Session layer
The session layer is responsible for dialog control and synchronization.

## Slide 20: Presentation layer
It is concerned with the syntax and semantics of the information exchanged between two systems
The presentation layer is responsible for translation, compression, and encryption.

## Slide 21: Application layer
The application layer is responsible for providing services to the user.
Functionalities are FTAM-File transfer &access management, Mail services and Directory services

## Slide 22: Summary of layers

## Slide 23: TCP/IP PROTOCOL SUITE
The layers in the TCP/IP protocol suite do not exactly match those in the OSI model. The original TCP/IP protocol suite was defined as having four layers: host-to-network, internet, transport, and application. However, when TCP/IP is compared to OSI, we can say that the TCP/IP protocol suite is made of five layers: physical, data link, network, transport, and application.

## Slide 24: WHY TCP/IP PROTOCOL SUITE
OSI doesn't define any particular protocol.
The session layer, which is used for session management, and the presentation layer, which deals with user interaction, aren't as useful as other layers in the OSI model.
.

## Slide 26: TCP/IP and OSI model

## Slide 27: ADDRESSING
Four levels of addresses are used in an internet employing the TCP/IP protocols:
  Physical address
    Ex. Ehternet address, machine address
  Logical address
    IP address
  Port number
  Specific
    URL, Email address, domain name

## Slide 28: Network layer in TCP/IP
Address resolution
Reverse address resolution
Internet control message
Internet group message

## Slide 29: Transport layer in TCP/IP
User Datagram Protocol (UDP)
  Connectionless, unreliable
Transmission Control Protocol (TCP)
  Connection-oriented, reliable
Stream Control Transmission Protocol (SCTP)
  For supporting multimedia and VOIP

## Slide 30: Relationship of layers and addresses in TCP/IP

## Slide 31: Example 2.1
In Figure a node with physical address 10 sends a frame to a node with physical address 87. The two nodes are connected by a link (bus topology LAN). As the figure shows, the computer with physical address 10 is the sender, and the computer with physical address 87 is the receiver.

## Slide 32: Physical addresses
The physical addresses will change from hop to hop,
but the logical addresses usually remain the same.

## Slide 33: TCP/IP in a Network
IP
(1,2)
NI
3487
data
data
1,2
data
3487
IP
(1,3)
NI
6537
data
1,3
6537
data
1,2
1,3

## Slide 34: Protocol Data Units PDU
PDUs are named according to the protocols of the TCP/IP suite:data, segment,packet ,frame and bits
Application layer – Data
Transport layer – Segment
Network layer – Packet
Data link layer – Frame
Physical layer - Bits

## Slide 36: Example 2.2
As we will see in Chapter 13, most local-area networks use a 48-bit (6-byte) physical address written as 12 hexadecimal digits; every byte (2 hexadecimal digits) is separated by a colon, as shown below:
  07:01:02:01:2C:4B

## Slide 37: Example 2.3
Figure 2.20 shows a part of an internet with two routers connecting three LANs. Each device (computer or router) has a pair of addresses (logical and physical) for each connection. In this case, each computer is connected to only one link and therefore has only one pair of addresses. Each router, however, is connected to three networks (only two are shown in the figure). So each router has three pairs of addresses, one for each connection.

## Slide 38: IP addresses

## Slide 39: TCP/IP thru a Router
IP
(1,2)
NI
3487
data
data
1,2
data
3487
IP
(2,5)
NI
3903
data
NI
6543
NI
1002
IP
(1,1) (2,3)
2,5
data
1,2
2,5
data
1,2
2,5
6543
data
1002
3903
Host A
Router
Host B

## Slide 40: Example 2.4
Figure 2.21 shows two computers communicating via the Internet. The sending computer is running three processes at this time with port addresses a, b, and c. The receiving computer is running two processes at this time with port addresses j and k. Process a in the sending computer needs to communicate with process j in the receiving computer. Note that although physical addresses change from hop to hop, logical and port addresses remain the same from the source to destination.

## Slide 41: Port addresses

## Slide 42: Example 2.5
As we will see in Chapter 23, a port address is a 16-bit address represented by one decimal number.