## Slide 1: Checksums
Idea: sum up data in N-bit words
  Widely used in, e.g., TCP/IP/UDP
Stronger protection than parity
1500 bytes
16 bits

## Slide 2: Internet Checksum
Sum is defined in 1s complement arithmetic (must add back carries)
  And it’s the negative sum
“The checksum field is the 16 bit one's complement of the one's complement sum of all 16 bit words …” – RFC 791
Notes: Give example of 5 and -5 in 1s and 2s complement

## Slide 3: Internet Checksum (2)
Sending:
Arrange data in 16-bit words
Put zero in checksum position, add
Add any carryover back to get 16 bits
Negate (complement) to get sum
0001
f203
f4f5
f6f7
+(0000)
------
2ddf0
ddf0
+ 2
------
ddf2
220d
Notes: Work through example

## Slide 4: Internet Checksum (3)
Sending:
Arrange data in 16-bit words
Put zero in checksum position, add
Add any carryover back to get 16 bits
Negate (complement) to get sum
0001
f203
f4f5
f6f7
+(0000)
------
2ddf0
ddf0
+ 2
------
ddf2
220d

## Slide 5: Internet Checksum (4)
Receiving:
Arrange data in 16-bit words
Checksum will be non-zero, add
Add any carryover back to get 16 bits
Negate the result and check it is 0
0001
f203
f4f5
f6f7
+ 220d
------
2fffd
fffd
+ 2
------
ffff
0000
Notes: Work through example

## Slide 6: Internet Checksum (5)
Receiving:
Arrange data in 16-bit words
Checksum will be non-zero, add
Add any carryover back to get 16 bits
Negate the result and check it is 0
0001
f203
f4f5
f6f7
+ 220d
------
2fffd
fffd
+ 2
------
ffff
0000

## Slide 7: Internet Checksum (6)
How well does the checksum work?
  What is the distance of the code?
  How many errors will it detect/correct?
What about larger errors?
Notes: Dist is 2, so fooled by 2 errors. But handles bursts up to 16 errors for a 16 bit checksum, and large errors ½^16

## Slide 8: Error Detection in Practice
CRCs are widely used on links
  Ethernet, 802.11, ADSL, Cable …
Checksum used in Internet
  IP, TCP, UDP … but it is weak
Parity
  Is little used