## Slide 1: IP HEADER FORMAT

## Slide 24
IPv4 has a 32-bit address length | IPv6 has a 128-bit address length
It Supports Manual and DHCP address configuration | It supports Auto and renumbering address configuration
In IPv4 end to end, connection integrity is Unachievable | In IPv6 end-to-end, connection integrity is Achievable
It can generate 4.29×109 address space | The address space of IPv6 is quite large it can produce 3.4×1038 address space
The Security feature is dependent on the application | IPSEC is an inbuilt security feature in the IPv6 protocol
Address representation of IPv4 is in decimal | Address Representation of IPv6 is in hexadecimal
Fragmentation performed by Sender and forwarding routers | In IPv6 fragmentation is performed only by the sender
In IPv4 Packet flow identification is not available | In IPv6 packet flow identification are Available and uses the flow label field in the header
In IPv4 checksum field is available | In IPv6 checksum field is not available
It has a broadcast Message Transmission Scheme | In IPv6 multicast and anycast message transmission scheme is available
In IPv4 Encryption and Authentication facility not provided | In IPv6 Encryption and Authentication are provided
IPv4 has a header of 20-60 bytes. | IPv6 has a header of 40 bytes fixed
IPv4 can be converted to IPv6 | Not all IPv6 can be converted to IPv4
IPv4 consists of 4 fields which are separated by addresses dot (.) | IPv6 consists of 8 fields, which are separated by a colon (:)
IPv4’s IP addresses are divided into five different classes. Class A , Class B, Class C, Class Da , Class E. | IPv6 does not have any classes of the IP address.
IPv4 supports VLSM(Variable Length subnet mask). | IPv6 does not support VLSM.
Example of IPv4: 66.94.29.13 | Example of IPv6: 2001:0000:3238:D