## Slide 1: Single Cycle Data path

## Slide 2: MIPS
MIPS (originally an acronym for Microprocessor without Interlocked Pipeline Stages) is a reduced instruction set computer (RISC)
Single-cycle implementation also called single clock cycle implementation.
An implementation in which an instruction is executed in one clock cycle.
While easy to understand, it is too slow to be practical.
Separate memories for instruction and data
Instruction Size – 32B, word length – 1B

## Slide 3: MIPS Instruction Format
d. Instruction format for the jump instruction (opcode = 2)

## Slide 4: Classes of Instructions
Memory-reference
Arithmetic-logical
Branches

## Slide 5: Introduction
For every instruction, the first two steps are identical:
  Send the program counter (PC) to the instruction memory and fetch the instruction from that memory.
  Read one or two registers, using fields of the instruction to select the registers to read. For the load word instruction, we need to read only one register, but most other instructions require reading two registers.

## Slide 6: Introduction
After these two steps, the actions required to complete the instruction depend on the instruction class.
Fortunately, for each of the three instruction classes (memory-reference, arithmetic-logical, and branches), the actions are largely the same, independent of the exact instruction.
For example, all instruction classes, except jump, use the arithmetic-logical unit (ALU) after reading the registers.

## Slide 7: Use of ALU in various classes of instructions
The memory-reference instructions use the ALU for an address calculation
The arithmetic-logical instructions for the operation execution
Branches for comparison.

## Slide 8: Actions after using ALU
After using the ALU, the actions required to complete various instruction classes differ.
A memory-reference instruction will need to access the memory either to read data for a load or write data for a store.
An arithmetic-logical or load instruction must write the data from the ALU or memory back into a register.
Lastly, for a branch instruction, we may need to change the next instruction address based on the comparison; otherwise, the PC should be incremented by 4 to get the address of the next instruction.

## Slide 9: Data Path for fetching instructions and incrementing the program counter
Memory Unit
PC
Adder to increment PC

## Slide 10: R-format instructions
They all read two registers, perform an ALU operation on the contents of the registers, and write the result to a register.
We call these instructions either R-type instructions or arithmetic-logical instructions
This instruction class includes add, sub, AND, OR and SLT (Set on Less Than)

## Slide 11: Arithmetic and Logical Operations
The two elements needed to implement R-format ALU operations are the register file and the ALU

## Slide 12: Memory Instructions
The two units needed to implement loads and stores, in addition to the register file and ALU, are the data memory unit and the sign extension unit.

## Slide 13: Branch Instruction
The beq (Branch if equal) instruction has three operands, two registers that are compared for equality, and a 16-bit off set used to compute the branch target address relative to the branch instruction address.
Its form is beq $t1,$t2,offset.
To implement this instruction, we must compute the branch target address by adding the sign-extended offset field of the instruction to the PC.
MIPS instructions are 32 bits = 4 bytes, so the branch offset is specified as a multiple of 4, i.e. a branch offset of 1 = 4 bytes.

## Slide 14: Branch Instructions
The datapath for a branch uses
  The ALU to evaluate the branch condition
  A separate adder to compute the branch target as the sum of the incremented PC and the sign-extended, lower 16 bits of the instruction (the branch displacement),
  shifted left 2 bits. (increases the effective range of the offset by a factor of 4.

## Slide 15: Single Cycle Datapath
Now that we have examined the datapath components needed for the individual instruction classes, we can combine them into a single datapath and add the control to complete the implementation.
This simplest datapath will attempt to execute all instructions in one clock cycle.
This means that no datapath resource can be used more than once per instruction, so any element needed more than once must be duplicated.
We therefore need a memory for instructions separate from one for data.
To share a datapath element between two different instruction classes, we may need to allow multiple connections to the input of an element, using a multiplexor and control signal to select among the multiple inputs.

## Slide 16: Building a Datapath
The operations of arithmetic-logical (or R-type) instructions and the memory instructions datapath are quite similar.
The key differences are the following:
  The arithmetic-logical instructions use the ALU, with the inputs coming from the two registers.
  The memory instructions can also use the ALU to do the address calculation, although the second input is the sign extended 16-bit off set field from the instruction.
The value stored into a destination register comes from the ALU (for an R-type instruction) or the memory (for a load).

## Slide 17: The datapath for the memory instructions and the R-type instructions.

## Slide 18: The simple datapath for the core MIPS architecture combines the elements required by different instruction classes.

## Slide 19: Control Unit
Multiple levels of decoding—that is, the main control unit generates the ALUOp bits, which then are used as input to the ALU control that generates the actual signals to control the ALU unit
Using multiple levels of control can reduce the size of the main control unit.
Using several smaller control units may also potentially increase the speed of the control unit.
Such optimizations are important, since the speed of the control unit is often critical to clock cycle time.

## Slide 20: ALU Control Lines to perform Arithmetic and Logical functions

## Slide 21: How the ALU control bits are set depends on the ALUOp control bits and the different function codes for the R-type instruction.

## Slide 22: MIPS Instruction Format
d. Instruction format for the jump instruction (opcode = 2)

## Slide 23: The datapath with all necessary multiplexors and all control lines identified.

## Slide 24: The effect of each of the seven control signals

## Slide 25: The simple datapath with the control unit

## Slide 26: The setting of the control lines is completely determined by the opcode fields of the instruction

## Slide 27: The setting of the control lines is completely determined by the opcode fields of the instruction
The first row of the table corresponds to the R-format instructions (add, sub, AND, OR, and slt).
For all these instructions, the source register fields are rs and rt, and the destination register field is rd; this defines how the signals ALUSrc and RegDst are set.
Furthermore, an R-type instruction writes a register (Reg-Write = 1), but neither reads nor writes data memory.
The ALUOp field for R-type instructions is set to 10 to indicate that the ALU control should be generated from the funct field.

## Slide 28: Control Lines for Load and Store
The second and third rows of this table give the control signal settings for lw and sw.
These ALUSrc and ALUOp fields are set to perform the address calculation.
The MemRead and MemWrite are set to perform the memory access.
Finally, RegDst and RegWrite are set for a load to cause the result to be stored into the rt register.

## Slide 29: Control Lines for Branch Instruction
The branch instruction is similar to an R-format operation, since it sends the rs and rt registers to the ALU.
When the Branch control signal is 0, the PC is unconditionally replaced with PC + 4; otherwise, the PC is replaced by the branch target if the Zero output of the ALU is also high.
The ALUOp field for branch is set for a subtract (ALU control = 01), which is used to test for equality.
Notice that the MemtoReg field is irrelevant when the RegWrite signal is 0: since the register is not being written, the value of the data on the register data write port is not used.
Thus, the entry MemtoReg in the last two rows of the table is replaced with X for don’t care.
Don’t cares can also be added to RegDst when RegWrite is 0.
This type of don’t care must be added by the designer, since it depends on knowledge of how the datapath works.

## Slide 30: The datapath in operation for an R-type instruction, such as add $t1,$t2,$t3

## Slide 31: The datapath in operation for a load instruction

## Slide 32: The datapath in operation for a branch-on-equal instruction

## Slide 33: The control function for the simple single-cycle implementation is completely specified by this truth table.

## Slide 34: Why a Single-Cycle Implementation Is Not Used Today
Although the single-cycle design will work correctly, it would not be used in modern designs because it is inefficient.
To see why this is so, notice that the clock cycle must have the same length for every instruction in this single-cycle design.
Of course, the longest possible path in the processor determines the clock cycle.
This path is almost certainly a load instruction, which uses five functional units in series: the instruction memory, the register file, the ALU, the data memory, and the register file.
Although the CPI is 1, the overall performance of a single-cycle implementation is likely to be poor, since the clock cycle is too long.
Suitable for RISC but not for CISC and floating point unit.

## Slide 35: Single Cycle Data Path using Pipeline Stages

## Slide 36: Multicycle Datapath

## Slide 37: Multicycle Datapath
The division of an instruction into five stages means a five-stage pipeline, which in turn means that up to five instructions will be in execution during any single clock cycle.

## Slide 38: The pipelined version of the Single Cycle datapath

## Slide 39: Instruction fetch Stage for Load and Store Instruction
The instruction being
read from memory using the address in the PC and then being placed in the
IF/ID pipeline register. Th e PC address is incremented by 4 and then written
back into the PC to be ready for the next clock cycle.

## Slide 40: Instruction Decode and Register File Read Stage
The instruction portion of the IF/ID pipeline register supplying the
16-bit immediate field, which is sign-extended to 32 bits, and the register
numbers to read the two registers. All three values are stored in the ID/EX
pipeline register, along with the incremented PC address.

## Slide 41: Execute or address calculation
The load instruction
reads the contents of register 1 and the sign-extended immediate from the
ID/EX pipeline register and adds them using the ALU.
That sum is placed in the EX/MEM pipeline register.

## Slide 42: Memory Access Stage for Load Instruction
The load instruction
reading the data memory using the address from the EX/MEM pipeline
register and loading the data into the MEM/WB pipeline register.

## Slide 43: Write Back Stage for Load Instruction
Reading
the data from the MEM/WB pipeline register and writing it into the register
file

## Slide 44: Control lines for Pipelined Datapath
Divide the control lines into five groups according to the pipeline stage.
Instruction fetch:
  The control signals to read instruction memory and to write the PC are always asserted, so there is nothing special to control in this pipeline stage.
Instruction decode/register file read:
  As in the previous stage, the same thing happens at every clock cycle, so there are no optional control lines to set.
Execution/address calculation:
  The signals to be set are RegDst, ALUOp, and ALUSrc.
  The signals select the Result register, the ALU operation, and either Read data 2 or a sign-extended immediate for the ALU.

## Slide 45: Control lines for Pipelined Datapath
Memory access:
  The control lines set in this stage are Branch, MemRead, and MemWrite.
  The branch equal, load, and store instructions set these signals, respectively.
  PCSrc selects the next sequential address unless control asserts Branch and the ALU result was 0.
Write-back:
  The two control lines are MemtoReg, which decides between sending the ALU result or the memory value to the register file, and Reg-Write, which writes the chosen value.

## Slide 46: Control lines for Pipelined Datapath

## Slide 47: The values of the control lines have been shuffl ed into three groups corresponding to the last three pipeline stages

## Slide 48: The Control lines for the Final three stages

## Slide 49: The pipelined datapath with the control signals connected to the control portions of the pipeline registers.

## Slide 50: References
David A. Patterson and . John L. Hennessy “Computer Organization and Design-The Hardware/Software Interface” 5th edition, Morgan Kaufmann, 2011.