## Slide 1: Control unit
Control unit
Provides control signals for the operation and coordination of all processor components.
  Is at the heart of the processor
Manages the computer’s resources and orchestrates the performance of its functional parts in response
to those instructions
System
bus
Main
memory
I/O
CPU
Internal
bus
ALU
Registers
Control
unit
CPU
Control unit
Registers &
decoders
Sequencing
logic
Control
memory
CONTROL UNIT

## Slide 2: Control unit
control unit
Inputs and Outputs
Control
unit
Instruction register
Control bus
Control signals with CPU
Control signals from control bus
Control signals to control bus
Flags
Clock
Inputs
  Instruction register
  Flags
  Clock
  Control signals from
  control bus
Outputs
  Control signals within
  the processor
  Control signals to control
  bus
Control
unit
Instruction register
Control bus
Control signals within CPU
Control signals from control bus
Control signals to control bus
Flags
Clock

## Slide 3: Control unit inputs
Clock
  This is how the control unit “keeps time.” The control unit causes one micro-operation (or a set of simultaneous micro-operations) to be performed for each clock pulse.
  This is sometimes referred to as the processor cycle time, or the clock cycle time.
Instruction register
  The opcode and addressing mode of the current instruction are used to determine which micro-operations to perform during the execute cycle
control unit
Inputs and Outputs
  Inputs
    Clock
    Instruction Register

## Slide 4: Control unit inputs
Flags
  These are needed by the control unit to determine the status of the processor and the outcome of previous ALU operations.
  For example
    for the increment-and-skip-if-zero (ISZ) instruction, the control unit will increment the PC if the zero flag is set.
Control signals from control bus
  The control bus portion of the system bus provides signals to the control unit
control unit
Inputs and Outputs
  Inputs
    Clock
    Instruction Register
    Flags
    Control signals from control bus

## Slide 5: Control unit outputs
Control signals within the processor
  These are two types
    Those that cause data to be moved from one register to another, and
    Those that activate specific ALU functions.
Control signals to control bus
  These are also of two types
    Control signals to memory and
    Control signals to the I/O modules
control unit
Inputs and Outputs
  Inputs
    Clock
    Instruction Register
    Flags
    Control signals from control bus
  Outputs
    Control signals within the processor
    Control signals to control bus

## Slide 6: Implementation of Control unit
Several approaches to the implementation of the control unit.
Most of these fall into one of two categories
  Hardwired implementation
  Microprogrammed implementation
Hardwired Control Unit
  In a hardwired implementation, the control unit is essentially a state machine circuit.
  Its input logic signals are transformed into a set of output logic signals, which are the control signals
Control Unit (C.U.)
Inputs and Outputs
  Inputs
    Clock
    Instruction Register
    Flags
    Control signals from control bus
  Outputs
    Control signals within the processor
    Control signals to control bus
Implementation of CU
  Hardwired
  Micro Programmed

## Slide 7: Use of Data Path Conditions in Control Signal Logic
Control Unit
Use of Data Path Conditions in Control Signal Logic
T0.
T1.
T2.
Step
Control Sequence
T3.
T4.
T5.
Step
Control Sequence
Control Sequence
T3.
T4.
T5.
Step
Control Sequence
Control Sequence
addi
shr
T6.
T7.
add
st
Example: Grc= T4.add+T4.(n=0).shr+…
AND
OR Gate
T1.
T5.
add
T5.
addi
T5.
st
T6.
shr
T7.
shr
Boolean Expression

## Slide 8: Use of Data Path Conditions in Control Signal Logic
Control Unit
Use of Data Path Conditions in Control Signal Logic
add
addi
shr
st
AND
OR Gate

## Slide 9: Generation of the logic for PCin and Gra
Control Unit (C.U.)
Inputs and Outputs
  Inputs
  Outputs
Implementation of CU
  Hardwired
  Micro Programmed
Hardwired Control Unit
  Control sequence
  Boolean expression for control signal
  Circuitry design for control signal Cout
    Examples
add
addi
Cout
Gra
T1
T5
add
T5
T7
Id
add
addi
Cout
Gra
T1
T5
add
T5
T7
Id

## Slide 10: Overview of Control Unit
Control Unit (C.U.)
Inputs and Outputs
  Inputs
  Outputs
Implementation of CU
  Hardwired
  Micro Programmed
Hardwired Control Unit
  Control sequence
  Boolean expression for control signal
  Circuitry design for control signal Cout
    Examples
  Overall view of C.U.
Counter
control
step
decoder
Clocking logic
Enable
Countin
Step generator
4
Interrupts and other external signals
OpCode
IR
Other signals from the data path
Decoder
Start
Master
Clock
Wait
Done
Load
Reset
Control Signal
encoder

## Slide 11: Pros and Cons of Hardwired control unit
Control Unit (C.U.)
Inputs and Outputs
  Inputs
  Outputs
Implementation of CU
  Hardwired
  Micro Programmed
Hardwired Control Unit
  Control sequence
  Boolean expression for control signal
  Circuitry design for control signal Cout
    Examples
  Overall view of C.U.
  Pros & Cons
Pros
Hardwired Control Unit is fast since it use of combinational circuits to generate signals
It depends on number of gates, how much delay can occur in generation of control signals
Cons
The complexity of the design increases as we require more control signals to be generated (need of more encoders & decoders)
Modifications in the control signals are very difficult because it requires rearranging of wires in the hardware circuit
It can be optimized to produce the fast mode of operation
Faster than micro- programmed control unit
Adding a new feature is difficult & complex
Difficult to test & correct mistakes in the original design
It is Expensive
RISC processors, with their simpler instruction format, typically use hardwired control units

## Slide 12: Summary
Control Unit (C.U.)
Inputs and Outputs
  Inputs
    Clock
    Instruction Register
    Flags
    Control signals from control bus
  Outputs
    Control signals within the processor
    Control signals to control bus
Implementation of CU
  Hardwired
  Micro Programmed
Hardwired Control Unit
  Control sequence
  Boolean expression for control signal
  Circuitry design for control signal Cout
    Examples
  Overall view of C.U.
  Pros & Cons

## Slide 13: Homework
Develop Boolean expressions for every control signals and implement Control Signal Logic
T0.
T1.
T2.
Step
Control Sequence
T3.
T4.
T5.
Step
Control Sequence
Control Sequence
T3.
T4.
T5.
Step
Control Sequence
Control Sequence
addi
shr
T6.
T7.
add
st
T5.

## Slide 14: References
Text Book
William Stallings “Computer Organization and architecture” Prentice Hall, 7th edition, 2006.

## Slide 15: Questions ?