## Slide 1: DMA - Problems
A hard disk with a transfer rate of 20 Mbytes/second is constantly transferring data to memory using
DMA. The processor runs at 300MHz, and takes 300 and 900 clock cycles to initiate and complete
DMA transfer respectively. If the size of the transfer is 20 Kbytes, what is the percentage of processor time consumed for the transfer operation?
Solution:
Step 1: Find Total Transfer Time
Transfer rate=20 MB per second = 20 × 220 bytes/sec
Data=20 KB=20 × 210 bytes
Time=(20 × 210)/(20 × 220)= 1 × 2-10 = 1 × 10-3 =1 ms
Step 2 :Find Processor Time
Processor speed= 300 MHz = 300 × 106 Cycles/sec
Cycles required by CPU for DMA Transfer =300+900 =1200 cycles Time=1200 cycles/(300 × 106) cycles/sec = 4 ×10 -6 sec = .004 ms
Step 3 : Find % of Processor Time
% Processor Time = (.004/1) × 100 = 0.4%
𝑻𝒐𝒕𝒂𝒍 𝑻𝒊𝒎𝒆 =
𝑻𝒐𝒕𝒂𝒍 𝑫𝒂𝒕𝒂
𝑻𝒐𝒕𝒂𝒍 𝑻𝒓𝒂𝒏𝒔𝒇𝒆𝒓 𝑹𝒂𝒕𝒆
𝑷𝒓𝒐𝒄𝒆𝒔𝒔𝒐𝒓 𝑻𝒊𝒎𝒆 =
𝑪𝒚𝒄𝒍𝒆𝒔 𝒇𝒐𝒓 𝑫𝑴𝑨 𝒕𝒓𝒂𝒏𝒔𝒇𝒆𝒓
𝑷𝒓𝒐𝒄𝒆𝒔𝒔𝒐𝒓 𝑺𝒑𝒆𝒆𝒅
% 𝑷𝒓𝒐𝒄𝒆𝒔𝒔𝒐𝒓 𝑻𝒊𝒎𝒆 =
𝑷𝒓𝒐𝒄𝒆𝒔𝒔𝒐𝒓 𝑻𝒊𝒎𝒆
𝑻𝒐𝒕𝒂𝒍 𝑻𝒊𝒎𝒆
× 100
Problem 1:
1 MHz = 106 cycles/sec

## Slide 2: DMA - Problems
A hard disk with a transfer rate of 10 Mbytes/second is constantly transferring data to memory using
DMA. The processor runs at 600MHz, and takes 300 and 900 clock cycles to initiate and complete
DMA transfer respectively. If the size of the transfer is 20 Kbytes, what is the percentage of processor time consumed for the transfer operation?
Solution:
Step 1: Find Total Transfer Time
Transfer rate=10 MB per second = 10 × 220 bytes/sec
Data=20 KB=20 × 210 bytes
Time=(20 × 210)/(10 × 220)= 2 × 2-10 = 2 × 10-3 = 2 ms
Step 2 :Find Processor Time
Processor speed= 600 MHz = 600 × 106 Cycles/sec
Cycles required by CPU for DMA Transfer =300+900 =1200 cycles Time=1200 cycles/(600 × 106) cycles/sec = 2 ×10 -6 sec = .002 ms
Step 3 : Find % of Processor Time
% Processor Time = (.002/2) × 100 = 0.1%
𝑻𝒐𝒕𝒂𝒍 𝑻𝒊𝒎𝒆 =
𝑻𝒐𝒕𝒂𝒍 𝑫𝒂𝒕𝒂
𝑻𝒐𝒕𝒂𝒍 𝑻𝒓𝒂𝒏𝒔𝒇𝒆𝒓 𝑹𝒂𝒕𝒆
𝑷𝒓𝒐𝒄𝒆𝒔𝒔𝒐𝒓 𝑻𝒊𝒎𝒆 =
𝑪𝒚𝒄𝒍𝒆𝒔 𝒇𝒐𝒓 𝑫𝑴𝑨 𝒕𝒓𝒂𝒏𝒔𝒇𝒆𝒓
𝑷𝒓𝒐𝒄𝒆𝒔𝒔𝒐𝒓 𝑺𝒑𝒆𝒆𝒅
% 𝑷𝒓𝒐𝒄𝒆𝒔𝒔𝒐𝒓 𝑻𝒊𝒎𝒆 =
𝑷𝒓𝒐𝒄𝒆𝒔𝒔𝒐𝒓 𝑻𝒊𝒎𝒆
𝑻𝒐𝒕𝒂𝒍 𝑻𝒊𝒎𝒆
× 100
Problem 2:
1 MHz = 106 cycles/sec

## Slide 3: Performance Metrics
Elapsed time/Response Time
The time between the start and completion of a task.
It includes time spent executing on the CPU, accessing disk and memory, waiting for I/O and other processes, and operating system overhead.
A useful number – but often not good for comparison purposes.

## Slide 4: Performance Metrics
CPU Execution Time/CPU Time/Processing Time
  Total time a CPU spends computing on a given task (excludes time for I/O or running
other programs).
  Doesn’t count waiting for I/O or time spent running other programs.
  User CPU time - CPU time spent in the program
  System CPU time - CPU time spent in the operating system
Throughput of a CPU/Bandwidth
  The total amount of work done in a given time.
  another measure of performance -number of tasks (Quantity) completed per unit time.

## Slide 5: Performance Metrics
MIPS
  Millions of instructions per second
MFLOPS
  Millions of floating point operations(FLO) per second

## Slide 6: Performance Metrics
To maximize performance, we want to minimize response time or execution time for task. Thus, we can relate performance and execution time for a computer X:
This means that for two computers X and Y, if the performance of X is greater than the performance of Y, we have
That is, the execution time on y is longer than X, so X is faster than Y.

## Slide 7: Performance Metrics - Example
PerformanceA = n × PerformanceB

## Slide 8: Performance Metrics - Example
Hint : Performance (X) < Performance (Y)
PerformanceX = n × PerformanceY

## Slide 9: Performance Metrics
For some program running on machine X,
Performance =
1
Execution time(X)
"X is n times faster than Y" – represented as
Performance(X) = n
Performance(Y)
Problem: Machine A runs a program in 20 seconds. Machine B runs the same program in 25 seconds. How many times faster is machine A?

## Slide 10: Computer Clock
Almost all computers are constructed using a clock that determines when events take place in the hardware.
These discrete time intervals are called clock cycles (ticks, clock ticks, clock periods, clocks, cycles).
Designers refer to the length of a clock period in time for a complete clock cycle (e.g., 250 picoseconds) and as the clock rate/frequency (e.g. 4 GHz, 5 MHz), which is the inverse of the clock period.
clock period

## Slide 11: Computer Clock
Clock cycle time - the amount of time for one clock period to elapse (e.g. 5 ns, 250 picoseconds….).
  Clock rate/frequency- inverse of the clock cycle time.
  For example, if a computer has a clock cycle time of 5 ns, the clock rate is:
1
---------------------- = 200 MHz
5 x 10-9 sec
clock period

## Slide 12: Processor Performance Equation
Performance Equation:
Alternatively
Also, execution time - depend on the number of instructions in a program
Execution time equals the number of instructions executed multiplied by the average time per instruction. Therefore, the number of clock cycles required for a program can be written as
Clock cycles per instruction (CPI), which is the average number of clock cycles for each instruction takes to execute, is often abbreviated as CPI.

## Slide 13: Processor Performance Equation
Since different instructions may take different amounts of time depending on what they do, CPI is an average of all the instructions executed in the program.
The basic performance equation can be rewritten in terms of instruction count, that is, number of instructions executed by the program, CPI and clock rate.

## Slide 14: Processor Performance Equation
To Summarize,
CPI (cycles per instruction)
A floating point intensive application might have a higher CPI
𝐶𝑙𝑜𝑐𝑘 𝑅𝑎𝑡𝑒 =
1
𝑐𝑙𝑜𝑐𝑘 𝑐𝑦𝑐𝑙𝑒 𝑇𝑖𝑚𝑒

## Slide 15: MIPS & MFLOPS

## Slide 16: Practice Problems
Example 1:
  CPU clock rate is 1 MHz
  Program takes 45 million cycles to execute
  What’s the CPU time?
45,000,000 * (1 / 1,000,000) = 45 seconds

## Slide 17: Practice Problems
Example 2:
  CPU clock rate is 500 MHz
  Program takes 45 million cycles to execute
  What’s the CPU time?
45,000,000 * (1 / 500,000,000) = 0.09 seconds

## Slide 18: Practice Problems
Example 3:
Suppose we have two implementations
of the same instruction set architecture (ISA).
  For some program,
    Machine A has a clock cycle time of 10 ns. and a CPI of 2.0
    Machine B has a clock cycle time of 20 ns. and a CPI of 1.2
Which machine is faster for this program, and by how much?
Assume that # of instructions in the program is 1,000,000,000.

## Slide 19: Practice Problems
Example 3: Solution
CPU / Execution TimeA = 109 * 2.0 * 10 * 10-9 = 20 seconds
CPU/ Execution TimeB = 109 * 1.2 * 20 * 10-9 = 24 seconds
= 24/20 = 1.2 times
Machine A is faster
Machine A has a clock cycle time of 10 ns. and a CPI of 2.0 Machine B has a clock cycle time of 20 ns. and a CPI of 1.2 # of instructions - 1,000,000,000.

## Slide 20: Practice Problems
Example 4:
Our favorite program runs in 10 seconds on computer A, which has a 2 GHz clock. We are trying to help a computer designer build a computer, B, which will run this program in 6 seconds. The designer has determined that a substantial increase in the clock rate is possible, but this increase will affect the rest of the CPU design, causing computer B to require 1.2 times as many clock cycles as computer A for this program. What clock rate should we tell the designer to target?

## Slide 21: Practice Problems
Example 4: Solution
A – Exec time = 10 sec, Clock rate – 2GHz B- Exec.time = 6 sec.
Clock cycle of B = 1.2 (clock cycle of A)
Find Clock rate of B?

## Slide 22: Practice Problems
Example 4: Solution
A – Exec time = 10 sec, Clock rate – 2GHz B- Exec.time = 6 sec.
Clock cycle of B = 1.2 (clock cycle of A)
Find Clock rate of B?

## Slide 23: Practice Problems
Example 5:
Suppose we have two implementations of the same instruction set architecture. Computer A has a clock cycle time of 250 ps and a CPI of
2.0 for some program, and computer B has a clock cycle time of 500 ps and a CPI of 1.2 for the same program. Which computer is faster for this program and by how much?

## Slide 24: Practice Problems
Example 5: Solution

## Slide 25: Average Cycles per Instruction
∑𝑛
Total CPI= 𝑖=1 𝑖
𝐼C ∗𝐶𝑃𝐼𝑖
Instruction count(Ic)

## Slide 26: Practice Problems
Example 6:

## Slide 27: Practice Problems
Example 6: Solution
B is faster
Since Clock cycle time is not given, we can estimate using CPU clock cycles itself

## Slide 28: Practice Problems
Example 6: Solution

## Slide 29: Practice Problems
Example 7:

## Slide 30: Practice Problems
Example 7: Solution

## Slide 31: With Frequency
CPI=
CPU clock cycles(c)
Instruction count(Ic)
∑𝑛
Total CPI= 𝑖=1 𝑖
𝐼C ∗𝐶𝑃𝐼𝑖
Instruction count(Ic)
The CPI is the average number of cycles per instruction.
If for each instruction type, we know its frequency and number of cycles need to execute it, we can compute the overall CPI as follows:
𝑖=1
CPI= ∑𝑛 Freq
i
∗ 𝐶𝑃𝐼
𝑖

## Slide 32: Practice Problems
Example 8: Solution
Let assume that a benchmark has 100 instructions:
  25 instructions are loads/stores (each take 2 cycles)
  50 instructions are adds (each takes 1 cycle)
  25 instructions are square root (each takes 50 cycles)
What is the CPI for this benchmark?
CPI = ((0.25 * 2) + (0.50 * 1) + (0.25 * 50))
= 13.5
CPI
Frequency
𝑖=1
CPI= ∑𝑛
Freqi ∗ 𝐶𝑃𝐼𝑖

## Slide 33: Practice Problems
Example 9:
Two different compilers are being tested for a 500 MHz. machine with three different classes of instructions: Class A, Class B, and Class C, which require one, two, and three cycles (respectively).
Both compilers are used to produce code for a large piece of software.
The first compiler's code uses 5 billions Class A instructions, 1 billion Class B instructions, and 1 billion Class C instructions.
The second compiler's code uses 10 billions Class A instructions, 1 billion Class B instructions, and 1 billion Class C instructions.
Which sequence will be faster according to MIPS?
Which sequence will be faster according to execution time?

## Slide 34: Practice Problems
Example 9: Solution
Clock rate – 500 MHz Cycles – class1-1 cycle,
class2-2 cycles, class3-3 cycles.

## Slide 35: Problems with Arithmetic Mean
For example, two machines timed on two benchmarks:
Average execution timeA = (2 + 12) / 2 = 7 seconds
Average execution timeB = (6 + 10) / 2 = 8 seconds
Weighted average execution timeA = 2*0.2 + 12*0.8 = 10 seconds Weighted average execution timeB = 6*0.2 + 10*0.8 = 9.2 seconds
 | Machine A | Machine B
Program 1 Program 2 | 2 seconds (20%) 12 seconds (80%) | 6 seconds (20%) 10 seconds (80%)

## Slide 36: MIPS rate
A common measure of performance for a processor is the rate at which instructions are executed, expressed as millions of instructions per second (MIPS), referred to as the MIPS rate.
Ic  Instruction count
T CPU time
fClock rate
CPI Cycles Per Instruction
𝐼𝑐 ∗ 𝑓
CPU clock cycles ∗ 106

## Slide 37: Practice Problems
Example 10:

## Slide 39: Practice Problems
Example 11:

## Slide 41
Example 12:
Assume that a benchmark has 100 instructions with the clock rate of 300Mhz. 20% instructions are loads/stores (each take 3 cycles), 40% instructions are adds (each takes 2 cycles), and 40% instructions are square root (each takes 60 cycles), what is the CPI and MIPS rate for this benchmark?
Ans: CPI=25.4 , MIPS=11.8

## Slide 42: MFLOPS
Floating-point performance is expressed as millions of floating-point operations per second (MFLOPS), defined as follows: