## Slide 1: FUNDAMENTALS OF FOG AND EDGE COMPUTING
Applications and Issues

## Slide 2: EXPLOITING FOG COMPUTING IN HEALTH MONITORING
AN ARCHITECTURE OF A HEALTH MONITORING IOT-BASED SYSTEM WITH FOG COMPUTING
Health monitoring IoT systems have to be reliable because their results indirectly or directly impact the medical doctor’s analysis and decisions.
An error or a delay in the results may lead to serious consequences, such as an incorrect treatment or a late response to the emergency, which may negatively affect human health.
A late notification from a human fall detection monitoring IoT system to a medical doctor can lead to a late response to a serious head injury, which quite possibly causes a death.
In this situation, if a medical doctor was informed about the case in real time, the doctor could provide first-aid procedures (e.g., stopping bleeding) to save the patient’s life.

## Slide 3
Health-monitoring IoT systems must provide high-quality data in real
time.
The latency requirements of e-health signals vary, depending on the characteristics of particular e-health signals.

## Slide 4
Maximum latency of EMG (Electromyogram) signals is less than 15.6 ms

## Slide 5
An architecture of the system with fog computing is shown in the below figure.
The system includes several primary components such as
  a sensor layer
  smart gateways with a fog layer
  cloud servers with end-user terminals.

## Slide 6
i) Device (Sensor) Layer
A device (sensor) layer consists of sensor nodes in which each node often has three primary components, including sensors, a micro- controller, and a wireless communication chip.
In some applications, an SD card can be integrated into a sensor node
for storing temporary data

## Slide 7
The sensors (e.g., ECG, glucose, SpO2, humidity, and temperature sensors) are used for collecting contextual data from surrounding environments and e-health data from a human body

## Slide 8
The contextual data such as room temperature, humidity, and statuses of the patient activities helps to improve the quality of e-health data and a doctor’s decisions.
For example, a heart rate of 100 beats/s of a healthy person will be normal when the person is running, whereas this rate will be high and problematic if he/she is resting on a chair.

## Slide 9
Collecting contextual data does not dramatically increase the burden of a sensor node in terms of weight, size, complexity, and energy consumption dramatically.
For example, the activity significances can be extracted from a single IC chip having 3-D accelerometer and 3-D gyroscope, while room temperature and humidity can be collected from another IC chip.
These chips are often small, lightweight, and energy efficiency.
The sensors often communicate with a micro-controller via one of the wire protocols such as Universal Asynchronous Receiver-Transmitter (UART), Serial Peripheral Interface (SPI), or Inter-Integrated Circuit (I2C).

## Slide 10
The micro-controller is often a low-power chip supporting sleep modes
and waking up methods.
The micro-controller’s frequency can vary depending on applications.
For example, an 8 MHz micro-controller can be used for collecting high-quality data from sensors and performing some light computation tasks (e.g., Advanced Encryption Standard – AES algorithm) while it still fulfills requirements of latency.
The micro-controller also communicates with a wireless chip via one of the mentioned wire methods.

## Slide 11
The wireless communication chip will vary depending on the applications’ requirements.
In general, low-power wireless protocols (e.g., BLE and 6LoWPAN) are more preferred for low data rate applications such as fall detection or heart rate monitoring because these protocols have a maximum bandwidth of 250 kbps.

## Slide 12
Wi-Fi is chosen for high-quality streaming applications (e.g., video surveillance or 24-channel EEG monitoring) where energy consumption is not the most important criteria.

## Slide 13
ii) Smart Gateways with Fog Computing
Fog computing can be described as a convergent network of interconnected smart gateways with fog services.
Depending on applications’ requirements, a smart gateway can be
movable or fixed in a specific place.
Each gateway type (i.e., mobile or fixed type) has its own advantages and disadvantages.
For example, a mobile gateway provides a mobility support but it has a
limited battery capacity and hardware resource constraints.

## Slide 14
A
fixed gateway is often
powerful
built from a
device supplied from
socket’s power.
The fixed
gateway can perform
computational tasks easily and
a wall
heavy
provide
more advanced services with high-quality data while a mobile gateway might not be able to perform the similar tasks.
In general, the fixed gateway is more preferred in many healthcare applications such as remote health-monitoring systems in the hospital and at home.

## Slide 15
Each smart gateway in a fog layer is an embedded device that often consists of three main components such as
  hardware
  an operating system
  software
Depending on specific health-monitoring applications and sensor nodes,
hardware can be various.
For instance, a smart gateway’s wireless communication chip is compatible with the wireless protocols (6LoWPAN, BLE, or Wi-Fi) used by sensor nodes.
A smart gateway can be equipped with a hard drive or an SD card for storing data and installing an operating system.
Although a storage capacity of the hard drive or an SD card is various, it
is often not very large (e.g., less than 128 GB).

## Slide 16
Lightweight operating systems are often preferred in smart gateways
because it does not require powerful hardware.
Lightweight versions of Linux kernels are used in many smart gateways.
The operating system provides a platform for installing useful software
resources more
easily and helps to manage tasks and hardware
efficiently and precisely.
Software in a smart gateway can consist of both
  Basic programs
  Fog services.
These programs
and services are designed for serving particular
applications’ requirements such as
Latency
Bandwidth
Interoperability.
Basic programs
provide fundamental features and functions of a
gateway such as
Data transmission
Gateway management
Basic levels of security.

## Slide 17
For example, IPtable, which is a lightweight and simple software installed in Ubuntu, is used for blocking unused communication ports of the gateway.
MySQL or MongoDB, which is an open-source database, can be installed in the smart gateway for flexibly, reliably, and efficiently managing databases

## Slide 18
Fog services
many advanced
enhancing the
services
quality
can consist of
for
of
healthcare service.
The services can help to
nodes
the burden of
for
reduce sensors extending lifetime
saving
their battery
the network
bandwidth
reducing the burden of cloud
informing emergent cases in real time.
For example, push notification for informing emergent is an important service of the fog

## Slide 19
iii) Cloud Servers and End-User Terminals
In general, there is not much difference between the cloud of a remote health-monitoring IoT systems having a fog layer and the cloud of other IoT applications without a fog layer (e.g., automation, education, and entertainment).
They all provide the fundamental features and basic services of a cloud
(e.g., data storage and data analysis).
The burdens of the cloud in IoT systems with a fog are less than in the IoT applications without a fog.
For instance, ECG feature extraction algorithms and machine-learning algorithms can be processed at a fog while the rest of the processing can be run on a cloud.
Results from the processing are updated in both the fog’s local storage
and the cloud.
A large amount of transmitted data can be saved and the cloud’s storage can be efficiently used.

## Slide 20
In general, a cloud of IoT systems with a fog is often customized for
supporting the fog services.
For example, in the IoT systems without a fog, cloud servers do not send data back to gateways.
In most of the cases, cloud servers simply transmit commands and
instructions to gateways, which are then forwarded to actuators.
Cloud servers in IoT systems with a fog also transmit data to smart gateways for serving some of the fog services such as mobility support.
In most of the conventional health-monitoring IoT systems, Web browsers, and mobile applications are the primary terminals of the health-monitoring IoT systems.
These terminals are often ease-to-use, popular, and suitable for most of the devices including smart devices (e.g., smart phone, Ipad) and computers (e.g., laptop and desktop).

## Slide 21
End users can access real-time data in human-readable forms (e.g., text
or graphical waveforms) via these terminals anytime and anywhere.
In some health-monitoring IoT systems, executable programs are used together with other terminals for accessing the monitored data.
For example, for reducing the risks from security attacks, end users have to use a virtual private network (VPN) and virtual platforms in order to use executable programs installed in the hospital’s system for accessing patient’s data.

## Slide 22: Smart Surveillance Video Stream Processing at the Edge for Real - Time Human Objects Tracking

## Slide 23: What is Edge Computing?
Edge computing refers to the practice of processing data near the edge of the network, where the data is generated, rather than in a centralized data-processing warehouse.
This approach reduces latency, conserves bandwidth, and improves response times, making it ideal for real-time applications like surveillance.

## Slide 24: Smart Surveillance
Smart surveillance systems use advanced technologies such as machine learning, artificial intelligence, and computer vision to analyze video streams in real-time.
These systems can detect, track, and analyze human objects, providing valuable insights for security, crowd management, and other applications.

## Slide 25: Real-Time Human Objects Tracking
Real-time human objects tracking involves detecting and following human figures within a video stream as they move.
This is crucial for applications like security monitoring, traffic management, and automated systems in smart cities.

## Slide 26
This diagram demonstrates how video data flows from cameras through preprocessing, human detection, and tracking stages, and finally to analysis, alert generation, and storage, with edge devices playing a crucial role in processing.

## Slide 27: Key Components
Video Data Acquisition: Cameras and sensors capture video data.
Data Preprocessing: Initial processing to enhance video quality and reduce noise.
Human Detection: Algorithms like Histogram of Oriented Gradients (HOG) and Support Vector Machines (SVM) are used to detect human figures.
Object Tracking: Techniques like Kernelized Correlation Filters (KCF) track the detected objects over time.
Edge Processing: All these steps are performed at the edge of the network, close to the data source, to ensure real-time processing.

## Slide 28: Video Data Acquisition
Types of Cameras and Sensors
Traditional CCTV Cameras: These are the standard cameras used in many surveillance systems. They provide continuous video feeds but often lack advanced processing capabilities.
IP Cameras: Internet Protocol (IP) cameras offer higher resolution and can be easily integrated into networked systems. They allow for remote access and control.
Thermal Cameras: These cameras capture infrared radiation, which is useful for detecting heat signatures, especially in low-light or nighttime conditions.
Smart Cameras: Equipped with built-in processors and memory, smart cameras can perform edge processing, reducing the need to send all data to a central server.
Multispectral Cameras: These capture information across different wavelengths, such as visible light and infrared, providing more detailed and comprehensive data.
LIDAR Sensors: Light Detection and Ranging (LIDAR) sensors use laser pulses to create high-resolution maps of the environment, which can be useful in tracking movement and identifying objects.

## Slide 29: Data Acquisition Process
Image Capture: The cameras and sensors continuously capture frames of video data.
Preprocessing: This step involves enhancing the video quality, such as adjusting brightness, contrast, and reducing noise. It may also include converting the raw data into a standard format.
Compression: To manage bandwidth and storage, the video data is often compressed using codecs like H.264 or H.265.
Transmission: The captured video is transmitted to storage devices or edge processors over wired or wireless networks. IP cameras, for example, transmit data over Ethernet or Wi-Fi.
Storage: Video data is stored on local storage devices or network-attached storage (NAS) systems. In edge computing, data can also be temporarily stored on the edge devices themselves.

## Slide 30: Data Preprocessing
Data Preprocessing involves enhancing video quality and reducing noise before further analysis.
This step is crucial for ensuring that the subsequent processes like human detection and object tracking are accurate and efficient.

## Slide 32: Human Detection
Human Detection involves identifying human figures within video frames. Two common algorithms used for this purpose are:
Histogram of Oriented Gradients (HOG)
  Description: HOG is a feature descriptor used to detect objects by analyzing the gradients in an image.
  Process:
    Compute gradients in the image to detect edges and corners.
    Create a histogram of these gradients.
    Use this histogram as a feature vector for detecting objects.
  Advantages: Effective for detecting humans in various poses and appearances.
Support Vector Machines (SVM)
  Description: SVM is a supervised learning model used for classification.
  Process:
    Use feature vectors (like HOG descriptors) to train the SVM classifier.
    The classifier learns to differentiate between human and non-human objects.
  Advantages: Highly accurate in distinguishing between different classes.

## Slide 33: Object Tracking
Object Tracking involves following the detected human objects as they move across video frames. One popular technique is:
Kernelized Correlation Filters (KCF)
  Description: KCF is a tracking algorithm that uses correlation filters.
  Process:
    Initialize the tracker with the object's position in the first frame.
    In subsequent frames, use correlation filters to find the object's new position.
  Advantages: Fast and efficient, suitable for real-time tracking.

## Slide 34: Edge Processing
Edge Devices: These are devices located close to the data sources (e.g., cameras, sensors) that perform local processing. Examples include smart cameras, edge servers, and IoT devices.
Edge Gateways: Gateways connect edge devices to the network and often provide additional processing power. They can also perform data aggregation and filtering before sending data to the cloud or central servers.

## Slide 35
Local Storage: Edge devices often have storage capabilities to temporarily hold data. This reduces the need for constant data transmission to central servers, conserving bandwidth and improving efficiency.
Processing Algorithms: Algorithms for data preprocessing, human detection, and object tracking are executed on the edge devices. This ensures real-time analysis and decision-making.

## Slide 36: Benefits
Reduced Latency: Processing data locally minimizes delays.
Bandwidth Conservation: Less data needs to be transmitted to the cloud.
Enhanced Privacy: Sensitive data can be processed locally without being sent to remote servers.
Scalability: Edge devices can be added as needed without overloading the network.

## Slide 37: Applications
Security: Real-time monitoring of public spaces, airports, and other sensitive areas.
Traffic Management: Analyzing pedestrian and vehicle flow in urban areas.
Smart Cities: Enhancing public safety and urban planning through intelligent surveillance.

## Slide 38: Conclusion
Data is captured and preprocessed at the edge.
Human figures are detected and tracked in real-time.
Local analysis and storage occur on edge devices.
Relevant data and alerts are transmitted to the cloud for further analysis or long-term storage.
Edge processing is a powerful approach that enhances the efficiency, speed, and security of data-intensive applications. By leveraging edge computing, smart surveillance systems can deliver real-time insights and actions, making them indispensable for modern security and monitoring solutions.

## Slide 39
https://www.youtube.com/watch?v=3uo1T8PYyQc